## Slide 1: Problem-1 2D-Truss problem

## Slide 2: Truss problem
4 m
20 k N
12 k N
A
B
C
D
E
F
G
H
1 b) Find the reaction force at support A and F
2 m
2 m
2 m
3 m

## Slide 3: Truss problem
Step-1
Identify the types of support in truss member

## Slide 4: Ladder problem
4 m
20 k N
12 k N
A
B
C
D
E
F
G
H
2 m
2 m
2 m
3 m
Roller support
Fixed support
Step-1
Identify the types of support in truss member

## Slide 5: Truss problem
Step-2
Apply support reaction force in truss member

## Slide 6: Truss problem
4 m
20 k N
A
12 k N
B
C
D
E
F
G
H
2 m
2 m
2 m
3 m
RFY
RFx
RAY
1. Roller support:
Only reaction force occur perpendicular to contact surface.
2. Fixed support :
Reaction force occur in horizontal and vertical direction both.
20 k N
12 k N
Free body diagram of entire truss member.
Step-3
Apply force and moment equilibrium conditions
a) Σ Fx = 0
b) Σ Fy = 0
c) Σ MP = 0
P is a point about which moment need to calculated. (You have to choose point P)

## Slide 7: Truss problem
4 m
A
B
C
D
E
F
G
H
2 m
2 m
2 m
3 m
RFY
RFx
RAY
20 k N
12 k N
Free body diagram of entire truss member.
1) Force equilibrium about
x- axis.
Σ Fx = 0
RFx = 0
2) Force equilibrium about
y –axis.
Σ Fy = 0
RAY + RFY = 32 KN.
3) Moment equilibrium about
point F.
RAY * FX ( ACW) + 20 kN * 3 m (ACW)= 0
RAY * 6 m + 20 KN * 3 m = 0
X
Line of action of force RAY
Perpendicular distance from F on line of action of force RAY
Y
Line of action
of force 20 kN
Perpendicular distance from F on line of action of force 20 KN act at point E.
RAY = - 10 KN

## Slide 8: Truss problem
RAY + RFY = 32 KN.
- 10 KN + RFY = 32 KN.
RFY = 42 KN.

## Slide 9: Truss problem
1 a) Determine the forces in all the members.
4 m
20 k N
12 k N
A
B
C
D
E
F
G
H
2 m
2 m
2 m
3 m
42 KN
-10 KN
Ɵ
Calculate angle (Ɵ)
In Δ ADF,
tan (Ɵ)
2. Calculate angle (Ⴔ)
In Δ DEF,
tan (Ⴔ) =
Ⴔ
=
p
b
tan (Ɵ) =
4
6
Ɵ = 33.690
p
b
tan (Ⴔ) =
4
3
Ⴔ = 53.130

## Slide 10: Truss problem
4 m
20 k N
12 k N
A
B
C
D
E
F
G
H
2 m
2 m
2 m
3 m
42 KN
-10 KN
Ɵ
Ⴔ
1 a) Calculate member force in all member.
Method of Joint
First we select a joint where only two member is connected.
Joint A ( AB and AH )
Joint E ( ED and EF)
2. Draw Free body diagram of
joint at E or A
(it is upto you which joint you wanted to draw first)
I will select Joint E.
FBD of Joint E
FEF
FED
E
Ⴔ
FED
FEF
20 k N
Y
X
Force equilibrium about x- axis
FED – FEF Cos(Ⴔ) = 0
Force equilibrium about y-axis
20 – FEF Sin (Ⴔ ) = 0
Solve this two equation find the force FED and FEF

## Slide 11: Truss problem
4 m
20 k N
A
12 k N
B
C
D
E
F
G
H
42 KN
-10 KN
Ɵ
Ⴔ
1 a) Calculate member force in all member.
Method of Joint
3. Select joint A. Draw Free body diagram of joint at A
FAH
Force equilibrium about x- axis
FAB + FAH Cos(Ɵ) = 0
Force equilibrium about y-axis
10 - FAH Sin (Ɵ ) = 0
Solve this two equation find the force FAH and FAB
-10 KN
FAB
FAH
Ɵ
Y
X
A
FED
FEF
FBH
FAB
FBC
FAB
FBC
FBH
Sin(90)
Sin(90)
Sin(180)
=
=

## Slide 12: Truss problem
4 m
20 k N
A
12 k N
B
C
D
E
F
G
H
42 KN
-10 KN
Ɵ
Ⴔ
1 a) Calculate member force in all member.
FAH
FED
FEF
FAB
FBC
FCG
FAH
FCH
Sin(Ⴔ)
Sin(180 -Ⴔ)
Sin(180)
=
=
FCG

## Slide 13: Truss problem
4 m
20 k N
A
12 k N
B
C
D
E
F
G
H
42 KN
-10 KN
Ɵ
Ⴔ
Method of Joint
4. Now select joint where only
two unknown member force.
Joint B ( FBC & FBH)
Joint F ( FEG & FFD)
Draw FBD at Joint B
FAH
FAB
FED
FEF
FAB
FBC
FBH
FEF
FFD
FFG
FAB
FBC
FBH
B
Force equilibrium about x- axis
FBC - FAB = 0
Force equilibrium about y-axis
FBH = 0
FAB is unknown to us So we can find FBC .

## Slide 14: Truss problem
4 m
20 k N
A
12 k N
B
C
D
E
F
G
H
42 KN
-10 KN
Ɵ
Ⴔ
Method of Joint
4 b) Joint F ( FEG & FFD)
Draw FBD at Joint F
FAH
FAB
FED
FEF
FAB
FBC
FBH
FEF
FFD
FFG
FAH
FHG = ??
FCH = ??
FFG
FFD
FEF
42 KN
900 - Ɵ
900 - Ⴔ
Draw FBD at Joint H
H
FAH
FHG = ??
FCH = ??
Ɵ
Δ ABH & Δ BCH are congruent.
Therefore angle C = angle A

## Slide 15: Thank you