## Slide 1: ESC-S201
21-oct
wed

## Slide 2: Friction Numerical

## Slide 3: Problem-3

## Slide 4: Ladder problem
3. A ladder of length 4 m weighing 200 N is placed against a vertical wall. The coefficient of friction between the wall and the ladder is 0.2. and that between the floor and the ladder is 0.3.The ladder in addition to its own weight has to support a man weighing 600 N. at a distance of 3m from A. Calculate the minimum horizontal force to be applied at A to prevent slipping.
600
A
B
200 N
C
600 N
AB = 4 m
AG = 2 m
AC = 3 m
G
P
AIM:
Pmin = ??

## Slide 5: Ladder problem
Step-1
DRAW FREE BODY DIAGRAM OF LADDER

## Slide 6: Ladder problem
Step-1
DRAW FREE BODY DIAGRAM OF LADDER
600
200 N
600 N
P
NB
VB
VA
A
B
At the time of slipping direction of velocity of point A and B are shown in above figure.
Velocity direction of point A and B.
Fs2
NA
Fs1

## Slide 7: Ladder problem
Step-2
Moment equilibrium about point A

## Slide 8: Ladder problem
600
200 N
600 N
P
NB
Fs2
NA
Fs1
Moment equilibrium about point A
Moment due to Normal force NB about point A.
= Force x perpendicular distance from A to line
of action of force NB
= NB x AX
= NB x AB * Cos( 300 )
= NB x 4 * Cos( 300 )
Direction : Anticlockwise moment
2. Moment due to Friction force Fs2 about point A.
= Force x perpendicular distance from A to line
of action of force Fs2
= Fs2 x AY
= Fs2 x AB Cos ( 600)
A
B
C
AB = 4 m
AG = 2 m
AC = 3 m
G
X
300
Y
= Fs2 x 4 x 0.5.
Direction: Anticlockwise direction.

## Slide 9: Ladder problem
600
200 N
600 N
P
NB
Fs2
NA
Fs1
Moment equilibrium about point A
3. Moment due to 600 N force act at point C about
point A.
= Force x perpendicular distance of line of action
of force 600 N from A.
= 600 N x AZ
= 600 N x 3 * Cos ( 600 ) m
= 900 N m
Direction : Clockwise moment
4. Moment due to 200 N force act at point G about
point A.
= Force x perpendicular distance of line of action
of force 200N from A.
A
B
C
AB = 4 m
AG = 2 m
AC = 3 m
G
X
300
Y
Z
= 200 N x AM
= 200 N x AG * Cos( 600)
= 200 N x 2 * 0.5 m
= 200 N m
Direction : Clockwise moment
M

## Slide 10: Friction problem
Moment equilibrium about point A
4 * NB * Cos( 300 ) (ACW) + 2 * Fs2 ( ACW) + 900 (CW) + 200 (CW) = 0
Take anti clockwise moment as positive.
4 * NB * Cos( 300 ) + 2 * Fs2 - 900 - 200 = 0
4 * NB * Cos( 300 ) + 2 * Fs2 = 1100
At the time of slipping friction force Fs2 = µB x NB
4 * NB * Cos( 300 ) + 2 * µB * NB = 1100
NB ( 4*Cos ( 300 ) + 2 * µB ) = 1100
NB ( 4*0.866 + 2 * 0.2 ) = 1100
NB ( 3.864) = 1100
NB = 284.7 N
600
A
B
µB
µB = Coefficient of friction between vertical wall and rod

## Slide 11: Friction problem
NB = 284.7 N
Fs2 = µB * NB
Fs2 = 0.2 * 284.7 N
Fs2 = 56.94 N
Step- 3
Force equilibrium about horizontal direction.
P + Fs1 = NB
P + µA NA = 284.7 N
P + 0.3 NA = 284.7 N - - - - - - (1)
Step-4
Force equilibrium about vertical direction
NA - 200 – 600 + Fs2 = 0
600
200 N
600 N
P
NB = 284.7 N
Fs2 = 56.94 N
NA
Fs1
NA - 200 – 600 + Fs2 = 0
NA - 200 – 600 + 56.94 = 0
NA = 743.06 N
By equation (1)
P + 0.3 NA = 284.7 N
P + 0.3*743.06 N = 284.7 N

## Slide 12: Friction problem
600
200 N
600 N
P
NB = 284.7 N
Fs2 = 56.94 N
NA
Fs1
P + 0.3*743.06 N = 284.7 N
P = 61.78 N