## Slide 1: ESC-S201
09-NOV
MON.

## Slide 2
Area moment of inertia

## Slide 3: Area moment of inertia
dA
dA is area of element
r
r is perpendicular distance of elemental area to axis about which area moment of inertia is calculated
Axis
Area moment of inertia ( I )
I = Area * r2
I = dA * r2

## Slide 4: Area moment of inertia
IYY = Σ dAi * x2i
Ixx = Σ dAi * y2i
Y
X
Area moment of inertia about x-axis
Area moment of inertia about x-axis
i = 1
i = n
i = 1
i = n
n tends to infinity.

## Slide 5: Area moment of inertia
Area moment of inertia
Mass moment of inertia
G
Centroidal axis
M
L
IG = M L2
12
G
Centroidal axis
A
L
IG = A L2
12

## Slide 6: Area moment of inertia
Area moment of inertia
Mass moment of inertia
G
Centroidal axis
IG = M R2
4
M
G
Centroidal axis
A
IG = A R2
4

## Slide 7: Area moment of inertia
Determine the moment of inertia of the section about an axis passing through the centroid
and parallel to the top most fiber of the section.
140
140
10
10

## Slide 8: Locate the centroid
Axis of symmetry
Centroid lie on axis of symmetry
Locus of G

## Slide 9: Locate the centroid
Centroid lie on axis of symmetry
Y- axis
X- axis
140
Section-1
70
G1
 | xG | yG
Section-1 | 0 | 70
O

## Slide 10: Locate the centroid
Centroid lie on axis of symmetry
Y- axis
X- axis
140
Section-2
 | xG | yG
Section-2 | 0 | 145
10
G2
O

## Slide 11: Locate the centroid
Centroid lie on axis of symmetry
Y- axis
X- axis
G2
O
Section | Area (mm2) | Centroid |  | Ai * xi ( mm3 ) | Ai * yi ( mm3 )
 |  | xc (mm) | yc (mm) |  | 
I | A1 | xG1 | yG1 | A1 * xG1 | A1 * yG1
 | 1400 | 0 | 70 | 0 | 9800
II | A2 | xG2 | yG2 | A2 * xG2 | A2 * yG2
 | 1400 | 0 | 145 | 0 | 203000
Section-1
 | xG | yG
Section-1 | 0 | 70
 | xG | yG
Section-2 | 0 | 145

## Slide 12: Locate the centroid
Y- axis
X- axis
O
Section | Area (mm2) | Centroid |  | Ai * xi ( mm3 ) | Ai * yi ( mm3 )
 |  | xc (mm) | yc (mm) |  | 
I | 1400 | 0 | 70 | 0 | 9800
II | 1400 | 0 | 145 | 0 | 203000
 | 2800 |  |  | 0 | 212800
Centroid of the Section | 
xG | yG
0 | 76
yG
212800
2800
=
G1
70
G
6

## Slide 13: Moment of inertia
Y- axis
G1
70
G
6
IG1
G2
IG = ( IG1 + A1 d12 ) + ( IG2 + A2 d22 )
d1
d2
IG

## Slide 14
G1
70
G
6
IG1
G2
d1
d2
IG
Section -1 |  |  |  |  |  |  | 
Length | width | Area | L1 | d1 | IG1 | A1d12 | IG1 + A1d12
140 mm | 10 mm | 1400 mm2 | 140 mm | YG – YG1 = 76 – 70 = 6 mm | (A1L12 )/12 = (1400* 1402 )/12 = 163566.67 mm4 | = 1400 x 6 = 8400 mm4 | = 171966.67 mm4
IG = ( IG1 + A1 d12 ) + ( IG2 + A2 d22 )
L1 =140
10
G1
70
IG1
G
6
IG