## Slide 1: Gas Chromatography
Introduction, theory, instrumentation, Carrier Gas
Dr. Nisha Sharma, Associate Professor, Pharmacy, C.S.J.M. University

## Slide 2: INTRODUCTION: GAS CHROMATOGRAPHY
Origin of gas chromatography: 1905, W. Ramsey
Separated mixture of gases and vapors
Used solid adsorbent: activated charcoal.
Gas used as mobile phase: introduced in 1952 by James and Martin.
The technique was based on a suggestion made 11 years earlier by Martin and Synge on partition chromatography
Martin and Synge were presented the Nobel Prize in chemistry in 1952.
Used to analyse volatile substances

## Slide 3
Partition takes place b/w gas & solid or gas & liq.
Nature of stationary phase– Fixed stat. phase-solid mat. like granular silica/alumina/C.---GSC
Fixed phase. Non vol. liq. Held as thin layer on solid support- (diatomacious earth or keisulguhr)--- GLC
GSC- limited application. Difficult to reproduce surface areas, excessive retention of active gases on solid surfaces which reduce available area, tailing of elution peaks.
GLC- Most imp. Widely used.
Principle: liq. Partition chrom. Mobile phase in gas liq. Chrom. is gas rather than liquid.

## Slide 4: Theory: Retention time
Time of emergence of peak max of a component after injection.
Sum of times the components spends in mobile phase (tM) & in stationary phase .
Adjusted Retention time t’R: time the component spends in stationary phase.
t’R=tR-tM
tM – measuring time to elute an unretained subs. Eg. Air or methane.

## Slide 6
TENTATIVE IDENTIFICATION OF UNKNOWN COMPOUNDS

## Slide 7: Retention Times

## Slide 8: INSTRUMENTATION: Gas Chromatograph
Filters/Traps
Air
Hydrogen
Gas Carrier
Column
gas system
inlet
column
detector
data system
Data system
Syringe/Sampler
Inlets
Detectors
Regulators
H
RESET
Basic Instrumentation:
1. Tank: of carrier gas 2. Injection port of sample
3. Column 4. Detector

## Slide 9
Schematic Diagram of Gas Chromatography

## Slide 10: Carrier gas:
He, H, N, Choice of gas-type of detector.
Additional regulating valves-for good control of pressure in inlet of column.
Gas- inert, available at low cost, should be suitable for detector & type of sample analysed, available in high purity, should not cause risk of fire or explosion hazard.
H- dangerous to use, better T.C., Low density, but may react with unsaturated compds & create a fire or explosive hazard.
He- 2nd best but explosive, gen used, good T.C. Inert, Low density, great flow rates.
N- inexpensive but low sensitivity
Air- used only when O in air is useful to the detector or separation.
Ex. H or He gives highest sensitivity with TCD because of difference in TC between organic mol. & H/He is greater than other gases