## Slide 1: 7th Semester Unit –IV Gas Chromatography
Introduction, theory, instrumentation, derivatization,
Temperature programming, advantages, disadvantages and applications
Dr. Nisha Sharma, Associate Professor, Pharmacy, C.S.J.M. University

## Slide 2: INTRODUCTION: GAS CHROMATOGRAPHY
Origin of gas chromatography: 1905, W. Ramsey
Separated mixture of gases and vapors
Used solid adsorbent: activated charcoal.
Gas used as mobile phase: introduced in 1952 by James and Martin.
The technique was based on a suggestion made 11 years earlier by Martin and Synge on partition chromatography
Martin and Synge were presented the Nobel Prize in chemistry in 1952.
Used to analyse volatile substances

## Slide 3
Partition takes place b/w gas & solid or gas & liq.
Nature of stationary phase– Fixed stat. phase-solid mat. like granular silica/alumina/C.---GSC
Fixed phase. Non vol. liq. Held as thin layer on solid support- (diatomacious earth or keisulguhr)--- GLC
GSC- limited application. Difficult to reproduce surface areas, excessive retention of active gases on solid surfaces which reduce available area, tailing of elution peaks.
GLC- Most imp. Widely used.
Principle: liq. Partition chrom. Mobile phase in gas liq. Chrom. is gas rather than liquid.

## Slide 4
Theory: Retention time

## Slide 5
TENTATIVE IDENTIFICATION OF UNKNOWN COMPOUNDS

## Slide 6: Retention Times

## Slide 7: INSTRUMENTATION: Gas Chromatograph
Filters/Traps
Air
Hydrogen
Gas Carrier
Column
gas system
inlet
column
detector
data system
Data system
Syringe/Sampler
Inlets
Detectors
Regulators
H
RESET
Basic Instrumentation:
1. Tank: of carrier gas 2. Injection port of sample
3. Column 4. Detector

## Slide 8
Schematic Diagram of Gas Chromatography

## Slide 9: Carrier gas:
He, H, N, Choice of gas-type of detector.
Additional regulating valves-for good control of pressure in inlet of column.
Gas- inert, available at low cost, should be suitable for detector & type of sample analysed, available in high purity, should not cause risk of fire or explosion hazard.
H- dangerous to use, better T.C., Low density, but may react with unsaturated compds & create a fire or explosive hazard.
He- 2nd best but explosive, gen used, good T.C. Inert, Low density, great flow rates.
N- inexpensive but low sensitivity
Air- used only when O in air is useful to the detector or separation.
Ex. H or He gives highest sensitivity with TCD because of difference in TC between organic mol. & H/He is greater than other gases

## Slide 10: Gas cylinder
High pressure gas cylinder (gas in compressed) – carrier gas reservoir.
Pressure regulator- To ↓ & control gas flow.
Soap bubble meter- To reproduce the rate of carrier gas.
Soap film is formed in path of gas when a rubber bulb containing aq sol of soap or detergent if squeezed. Time req for soap film to move b/w 2 graduations on burette is measured & converted to flow rate.

## Slide 11: Sample Introduction
Column inlet-sample port injector. Solute-chrom-Vapor state. Inj port is heated to temp-rapid vaporization, but no thermal degradation of solute
Construction of port- Heavy mass, maint at ↑Temp. Sample should be intro immediately into column.
Liq/gas sample- inj by syringe-0.1-100µL. Rapid inj. into gas stream.
Liq- injected- near- as solutions with syringe-0.5-10 µL.
Solid- dissolved in suitable solvent-injected as solution.
Injection of samples which can’t be vaporised at operating temp. are avoided. B’cos compds not move appreciably in liq or solid form may clog the port & damage the column.

## Slide 12: G.C INJECTION SYRINGE: * To rapidly vaporize the sample. * Slow vaporization ↑ses band broadening, by ↑sing the sample “plug”. * Injection port temperature mostly held 50°C higher than BP of least volatile compd.