## Slide 1: Electrophoresis Paper electrophoresis
Dr. NISHA SHARMA, ASSOCIATE PROFESSOR, C.S.J.M. UNIVERSITY, KANPUR

## Slide 2
TYPES OF ELECTROPHORESIS
Zone Electrophoresis
Paper E
Gel E
Moving Boundary Electrophoresis
Iso tacho-phoresis
Cellulose Acetate E
Capillary E
Isoelectric
Focussing
Immuno E
Migration of charged particles on supporting media
Migration of charged particles in solution. No supporting media

## Slide 3: PAPER ELECTROPHORESIS
Migration or separation of particles takes place along a filter paper
Sample is applied in the paper strip as circular spot / point
Whatman filter paper no. 1 and 3mm, 3 or 5 cm wide or cellulose acetate paper moistened with buffer
The end of paper is submerged in separate reservoir containing buffer & in this electrodes are fitted , current is passed, results in migration of ions towards oppositely charged electrodes
Separation- 12-14 hrs
Mainly used for separation of proteins
Serum proteins, Hb, Lipoproteins, Isozymes
Proteins are charged with NH2 & COOH groups
At pH > pI proteins → -ve charge → anode
Two types: Horizontal & vertical

## Slide 6: PAPER ELECTROPHORESIS

## Slide 8: Paper Electrophoresis
The charge carried by a molecule depends on the pH of the medium.
Electrophoresis at low voltage is not usually to separate low molecular weight compounds because of diffusion, but it is easier to demonstrate the relationship b/w charge and pH with amino acids than with proteins or other macromolecules”

## Slide 9: Apparatus
Power pack DC – 0-500 V or 0-150mA
Electrophoretic cell- electrodes, buffer reservoirs, transparent insulating cover etc.
Sample applications: spot/streak
Electrophoretic run: sample equillibrated with buffer
Over heating avoided by cold room
Paper dried @ 110°C
Detection : by comparing standards
Fluorescence , UV-absorption, staining

## Slide 10: Paper Electrophoresis
Apparatus: Consists of Power Pack and an Electrophoretic Cell.
Power pack provides stabilized DC & controls V & I out put, which have an out put of 0-500V and 0-150mA
The Electrophoretic cell has electrodes, buffer reservoirs, support for paper, supporting transparent insulating cover. The electrodes- made of platinum.
Filter paper: Paper of good quality, contain at least 95% α-cellulose, with very slight adsorption capacity.

## Slide 11: Paper Electrophoresis
Application of sample- as spot – 0.5cm dia
As a narrow uniform streak.
Sample- applied before the paper equilibration with buffer or after.
After sample application, equillibration of paper with buffer.
Current switched on.

## Slide 12: Buffers used
Separation | Buffer | pH | Ionic str. | Composition
Proteins | Barbital | 8.6 | 0.05 | 10.3 g Na-barbiturate 1.84g barbital
 | Phosphate | 7.4 | -- | 0.6g NaH2PO4H2O 2.2G Na2HPO4
Nucleoproteins | Acetate | 4.5 | 0.1 | 3.51g NaCl 3.28g Na-acetate pH-4.5 with HCl
 | Citrate | 4.5 | 0.13 | 28.46g Na-citrate 20.6g citric acid
Amino Acids | Phosphate | 4.6 | 0.15 | 20.4gKH2PO4
 | Michaelis | 8.6 | 0.1 | 9.8g sodium barbiturate

## Slide 13
Detection:
Unknown electrogram compared with std.
Individual components identified by physical properties
Fluorescence
Staining with Ethinium bromide, visualization under U.V. light – DNA, RNA
Flurescamine or Dansyl chloride staining- for amino-acids, peptides, proteins

## Slide 14
Detection:
U.V. Absorption: proteins, peptides, nucleic acids- absorbs- 260-280nm,
Quantitative determination
Applications:
Serum analysis for diagnostic purpose is routinely carried about by paper electrophoresis.
Muscle proteins, egg white proteins, milk proteins & snake, insect venom analysis done by this technique.

## Slide 15
Advantages: Economical, easy
Disadvantages: Time taking 14-16 hrs
Some compounds- proteins, hydrophillic molecules, can’t be resolved- adsorptive, ionogenic prop. of paper- tailing, distortion of component bands

## Slide 17: Cellulose acetate electrophoresis
Modified version of paper electrophoresis
Bacteriological acetate membrane filters are taken in place of regular chromatography paper
Advantages of cellulose acetate strips over paper
Chemically pure & free of lignin & hemicelluloses
low content of glucose, suitable for polysaccaharide electrophoresis
Not hydrophilic, so holds very little buffer so better resolution in short time
Applications: clinical investigation such as separation of glycoproteins, lipoproteins & haemoglobin from blood