## Slide 1: System
The materials on which we focus our attention
Subject of discussion or analysis
Material under consideration
Thermodynamic System
Definite quantity of matter bounded by some closed surface
A part of the universe which is selected for study and is separated from the rest of the universe by a definite boundary
System Properties
The choice of a system and its boundary is largely decided by convenience and not by any principle.
It is decided by the analyst depending on the particular problem at hand.

## Slide 2
The choice of the system may differ from person to person performing the analysis
The boundary surface may change in shape as well as in size when the system undergoes a change.
The boundary need not necessarily be real either it can be imaginary.
The quantity of the material constituting the system must remain constant (control mass system).
Surroundings
The combination of matter and space outside the system.
The material which is not included in the system boundary.
Rest of the universe, other than the system.

## Slide 3
Boundary or wall
By which system and its surroundings are separated
Movable wall – Allows to change in volume
Rigid Wall – Does not allows to change in volume
Diathermal Wall - Allows to change in energy (in the form of heat)
Adiabatic Wall – Does not allows to change in energy (in the form of heat)
Restrictive or nonrestrictive w.r.t. extensive parameters
The system can be made to under go a change by manipulating the nature of the wall enclosing the system.
A system enclosed by an adiabatic wall can exchange energy in the form of work with its surroundings.
A system enclosed by a rigid and adiabatic wall can not exchange energy either in the form of work or heat with its surroundings.

## Slide 4: Types of system
System can be classified either depending on
(a) Homogeneity or (b) Interaction with surroundings
Depending on homogeneity
(a) (i) Homogeneous system
  Completely uniform throughout (in all respect)
  Consists only one phase
  Ex- a pure solid or a liquid or a solution or a mixture of gases
  Not uniform throughout
  Consists two or more phases
  Ex- Mixture of two or more immiscible liquids, a solid in contact with a liquid in which it does not dissolve
(ii) Heterogeneous system

## Slide 5
Depending upon the interaction b/w the system and surrounding
(i) Open System
  Can exchange matter as well as energy with its surroundings.
  Ex- Hot liquid taken in a beaker
  Can exchange energy but not matter with its surroundings.
  Ex- Hot liquid taken in a closed metallic flask
  Can exchange neither energy nor matter with its surroundings.
  Ex- Hot liquid taken in a thermally insulated closed flask
  Open system – Both matter and energy are not constant
  Closed system – Matter remains constant but not energy
  Isolated system – Both matter and energy are constant
  no interaction b/w system 7 surroundings
(ii) Closed System
(ii) Isolated System

## Slide 6: Properties of a system
Extensive property – Depends upon the amount of substance present in the system.
Depend upon the size or extent
Ex- Volume, mass, internal energy, free energy, enthalpy, entropy, heat capacity
Intensive property – Does not depend upon the amount of substance present in the system.
Independent of the size or extent
Ex- Temperature, pressure, density, concentration, viscosity, refractive index, surface tension, specific heat, molar entropy, molar heat capacity
Specific volume = V/m, Specific internal energy = U/m
Molar volume = V/N, Molar internal energy = U/N
m-mass, N – Avogadro's number (mole number)