## Slide 1: Components of wheat mill:
Break roll-
It consists up of twin pair of corrugated steel rolls.
One roll of pair, rotates faster compare to the other roll.
The differential speed being 2.5 : 1.
Break shifting system -
Plain shifter ; it is a scalping syster, removing large bran pieces, adhering to the endosperm.
The next series which are finer, remove bran and germ.
PURIFIER : It consist of a long oscillating sieve inclined downward, thought it air current is passed.The milling containing finer bran particles are removed by purifier , before they move to the reduction room.
Reduction roll-
The reduction roll is comprised up for 2-smooth rolls, the rolls in the reduction system are further divided into coarse roll or fine roll. Depending upon clearance between the rolls.
These reduce the endosperm.

## Slide 2: 4. Reduction shifting system-
The same plain shifter is used here.
After each reduction, the product is separated by plain shifter, where finished floor is shifted by 120 mesh size and oversized material is sent back to reduction roll system for further processing.
5. Scratch system-
If the mill is not functioning properly, i.e. good release of endosperm is not obtained, then the scratch system is used.
It is the extension of break-roll system.
AIR CLASSIFICATION: Finished product from roller mill is further reduced in special grinders moving at high speed.

## Slide 3: BULGUR:
It is a cereal food made from the cracked parboiled whole grain (here wheat). Mainly from durum wheat.
It has nutty flavour.
It is used as a substitute for rice.
It can stored for 6-8 months under wide of temperature and humidity.
PROCESSING- Boil whole wheat in open vessels until it becomes tender.
Then the cooked wheat is spread in thin layers for drying in the sun.
Then the outer bran layers are removed by sprinkling with water and rubbing by hand. This is followed by cracking the grains by stones or in crude mill.

## Slide 4: FERINA:
It is a milled wheat , popular in US.
It is made from wheat middling- the germ and endosperm of the grain, which is milled and get fine consistency
It is carbohydrate rich food.
It is used as breakfast cereals abd also baby food.
Cream of wheat is a popular commercial Farina product.

## Slide 5: WHEAT BERRY:
It is row, unprocessed wheat kernel containing the bran and germ and endosperm.
These kernel will double in volume when cooked in water .
It have a nutty taste with tender texture.
WHEAT FLOUR:
Wheat flour is either white ( if bran and germ have been removed, only endosperm present ) or brown ( wholemeal flour containing bran, germ, and endosperm).
The flour is known as STRONG, if it has HIGH gluten content.
When the flour is SOFT, if the gluten content Low.