## Slide 1: Drying
Drying is the application of heat under controlled conditions to remove the majority of water normally present in the food by evaporation.

## Slide 2: Principle of preservation by Drying
Remove the water necessary for the growth of microbe and for the enzymatic activity.
Reduction in the water activity increases the osmotic pressure by increasing the concentration of sugar, salt and other solutes, thus creating the environment which is not favourable for the growth of microbes.

## Slide 3: Drying Curve

## Slide 4: Procedure
When the hot air is blown over a wet food, water vapour diffuses through a boundary film of air surrounding the food and is carried away by the moving air.
A water vapour pressure gradient is established from the moist interior of the food to the dry air. The boundary film acts as a barrier to both heat transfer and the removal of water vapour.
When water vapour leaves the surface of the food, it increases the humidity of the air in the boundary film. This reduces the water vapour pressure gradient and sows the rate of drying.

## Slide 5: Graph explanation
The drying of the food depends upon the relative humidity of the air, temperature of the air flowing through the food.
When the food is dried, it has the following phases:-
Initial settling stage
Here, there is no loss of moisture and the surface of food gets heated to the wet bulb temperature (A to B).

## Slide 6
2. Constant rate period
Here, the rate of loss of moisture from the surface of food is same as the rate at which the moisture moves to the surface of food from the interior of food and the drying process commences.
This process continues until the critical moisture content is reached.
The surface temperature of the food remains close to the wet bulb temperature of the drying period until the end of constant rate period, due to the cooling effect of evaporating water.

## Slide 7
3. Falling rate period
When the moisture content falls down the critical moisture content, the rate of drying drops until it reaches EMC i.e. Equilibrium Moisture Content.