## Slide 1: Forced Vibration

## Slide 2
F(t)
Aim: Derive the differential equation of motion of spring mass system subjected to external applied excitation force.
M
k
x
Forced Vibration

## Slide 3
First we define coordinate to specify
position of mass M. We choose a
coordinate fixed at natural length
of spring. Suppose position of mass M
is x at any instant of time t.
Draw free body diagram of mass M.
Fs is spring force.
F(t) is external applied time
varying force.
N is normal contact force.
Fs
F(t)
Mg
N
Forced Vibration
F(t)
M
k
x
3. Apply Newton second law of motion:
Σ Fx = m ax
m ẍ = F (t) – Fs
m ẍ + Fs = F(t)
m ẍ + k x = F(t)
This equation is known as differential
equation of motion (DEOM).

## Slide 4
Forced Vibration
m ẍ + k x = F(t) - - - - - (1)
Case – 1 :
F(t) is harmonic force
F(t) = F0 Sin (ω t)
F0 = Force Amplitude.
ω = exciting frequency
Equation (1) is second order
Non homogenous differential
Equation.
Solution of equation (1) is
x(t) = complementary / transient solution +steady state solution.
x(t) = xc (t) + xss (t).
For complementary solution:
m ẍc + k xc = 0
For steady state solution:
m ẍss + k xss = F0 Sin (ω t)

## Slide 5
Forced Vibration
For steady state solution:
m ẍss + k xss = F0 Sin (ω t)
Steady state solution take a
form xss (t) = X0 Sin(ω t – φ)
X0 = Displacement amplitude.
φ = Phase angle.
Substitute in above equation we
Get,
- m X0 ω2 Sin (ω t – φ) + k X0 Sin(ω t – φ) = F0 Sin (ω t)
( k – m ω2 ) X0 Sin(ω t – φ) = F0 Sin (ω t)

## Slide 6
Steady state solution
( k – m ω2 ) X0 Sin(ω t – φ) = F0 Sin (ω t)
After equating above equation we get,
(k – m ω2 ) X0 = F0
F0
(k – m ω2 )
φ = 00
Steady state solution:
xss (t) = X0 Sin(ω t)
Note : Phase angle is equal to zero.
X0 =

## Slide 7
Resonance condition
Take excitation frequency is equal to natural frequency.
If ω = ωn then displacement amplitude X0 is equal to infinity. So this condition is called as resonance.
Characteristic of resonance:
Spring mass system vibrate is larger amplitude then our structure
will fail.