## Slide 1: Blood Grouping Techniques Part -1
Dr Versha Prasad

## Slide 2
B GROUPING AND SUBGROUPING
Three manual methods can be used when performing blood grouping
1.Glass slide or white porcelain tile
2.Glass test tube
3.Microwell plate or microplate
Newer techniques –
•Column technique (sephadexgel)
•Solid phase tests

## Slide 3: Slide or Tile Method
This technique may be used for emergency ABO grouping tests or for
preliminary grouping particularly in an outdoor camp Slide or tile testing is
not recommended for routine use because it is not reliable for
weakly reactive antigens on cells
serum grouping with low titre anti A or anti B Disadvantages
Less sensitive than the tube test
Drying up of the reaction mixture can cause aggregation of cells giving
false positive results
Weaker reactions are difficult to interpret

## Slide 4: Microplate Technique
Microwell plate consists of a small tray with 96 small wells each of which
can hold about 200 300u1 of reagent.
Microplate technology is gaining widespread popularity due to increasing
workload in blood transfusion laboratories and recent availability of
packaged automated system.
Three types of microplates are available
a.U type well
b.V type well
c.Flat bottom
The U type well is generally used in red cell serological work as it is easier
to read the results in U bottom plates.

## Slide 5: Advantage of microplate ABO Grouping
1. Small volumes and low concentration of sera and red cells are used, making it cost effective
2. Easy handling of a microplate, which can replace 96 test tubes.
3. Batching of samples can be achieved with considerable economy in space and time.
4. If larger laboratories acquire microplate hardware items e.g. reagent dispenser, sample handler and cell washer it may further reduce the operation time.
5. Large batches of plates can be predispensed with antisera and reagent red cells before testing.
6. The technique of microplate grouping may be automated by on line data capture in larger laboratories, which may help in
a) reduction in reading and transcription errors
b) saving in staff time
c) use of bar codes for samples and microplate identification

## Slide 6: Advantage of microplate ABO Grouping
6. The technique of microplate grouping may be
automated by on line data capture in larger laboratories,
which may help in
a) reduction in reading and transcription errors
b) saving in staff time
c) use of bar codes for samples and microplate identification
d) integration into a comprehensive computer system for storage of data.

## Slide 7: Tube Method: Advantage of tube Method
Test tubes either of glass or plastic may be used. The tube technique is more sensitive than slide technique for ABO grouping.
Advantage
• It allows for fairly long incubation without drying up of the tubes contents.
• Centrifugation involved enhances the reaction allowing weaker antigens and antibodies to be detected.
• Simplicity of reading and grading of results .
• Clean and more hygienic.
• Requires smaller volume of reagents
• More sensitive than slide technique

## Slide 8: GROUPING BY TUBE METHOD
Samples
CPDA anti coagulated Blood samples collected from any source.
Reagents required for tube method
• Working standardised Monoclonal antisera (Anti A, Anti B,Anti A,B)
• Anti A1 (Lectin) & Anti H (Lectin)
• Reagent cells (A cells, B cells and O cells), 3% in Normal Saline.
• Test red cells Samples from IRCS
• Normal Saline (0.9%)

## Slide 9: Processing of blood samples Separation of RBC & Plasma
• Allow all reagents to come to Room Temperature
• Identify reagents RBC / blood samples to be used for reverse grouping
• Fill in proforma.
Processing
Centrifuge at 1000 rpm for 1 min at R.T using clean pipette tip, aspirate plasma gently without disturbing settled cells and transfer to a labeled clean test tube for reverse grouping

## Slide 10: Preparation of cell Suspension
• Label the tubes as per S.No . of samples
• Add 1ml whole blood in respective S.No . of tubes and Normal saline (N.S) 8 ml, mix well.
• Centrifuge at 2500 rpm for 3 min at R.T
• Aspirate supernatant & discard
• Wash 3 times as above till supernatant is clear.
• Consider cell pellet as 100%
• Prepare 3%red cells suspension in normal saline