## Slide 1: High Performance Liquid Chromatography (HPLC)
What is HPLC?
Types of Separations
Columns and Stationary Phases
Mobile Phases and Their Role in Separations
Injection in HPLC
Detection in HPLC
Variations on Traditional HPLC
  Ion Chromatography
  Size Exclusion Chromatography

## Slide 2: Theory of HPLC
20% of compds. Can be analyzed by GC. Because of non-volatility & thermal instability.
HPLC is not limited by sample volatility, Thermal stability. It can separate macromolecules, ionic sp., labile natural products, polymeric mat., high mol. Wt. polyfn., compds.,
Separation is due to specific interaction of sample mol., with stationary & mobile phase.

## Slide 3
Chromatographic terms
Baseline
Injection monitoring
Eluent peak; dead volume
Peak wide
Peak width
at half-height
Baseline noise
Peak fronting
Tailing
poor resolution
Shoulder
Baseline drift

## Slide 4
RP-HPLC – Variables
Alltech Chromatography Sourcebook, 2004-04 catalog

## Slide 5
Peak shape
Reason for bad peak shape
 bad column - caves, channels
 dead volume - void in column, external dead volume
 column overload
asymmetric peak shape
k´ changes with sample volume
 chemical tailing
polar compounds strongly interact with stat. Phase (often amines on C-18)
T= Asymmetry

## Slide 6
Schematic Presentation of a Chromatogram

## Slide 7
HPLC - Resolution
Resolution (RS) of a column provides a quantitative measure of its ability to separate two analytes
Rs = DZ /1/2(WA+WB)
Rs =

## Slide 8
HPLC - Resolution
Rs
Skoog and Leary: Principals of Instrumental Analysis, 4th ed. Suanders, 1992

## Slide 9
The theoretical plate number or N is a quantitative measure for the column efficiency
In formulas (1) or (2) the peak base width WB or the half width WH are compared with the retention time tR
Plate Number

## Slide 10
N is defined as square of ratio of retention time divided by standard deviation of the peak (s).
Plate Number
Relationship using width at half height is also used to calculate N as described in USP

## Slide 11: Plate Number and Plate Height
Since an efficient separation column delivers sharp peaks with narrow base widths or half widths, a better column has relatively high value of N, at equal retention time tR. The concept of the theoretical plates has its origin in the theory describing the efficiency of distillation. The concept of the theoretical plates is a useful tool to describe the efficiency of a separation column
The number of theoretical plates is proportional to the column length L. The longer a column, the more theoretical plates it has; however, the column back pressure increases. To be able to compare separation, columns of various lengths, the theoretical plate height, H is used.
H = L/N
Well packed columns at optimum flow rate have H values 2 - 5 times the particle diameter of the carrier substance. For a column of the length L = 100 mm, packed with 5 µm material, a theoretical plate height of 10 - 25 µm results.

## Slide 12
HPLC - Column Efficiency
Skoog and Leary: Principals of Instrumental Analysis, 5th ed. Suanders, 1998

## Slide 13
HPLC – Resolution vs Column Efficiency (N, H)
van Deemter Equation
H = A + B/u +(Cs + Cm)u
H = L / N
Skoog and Leary: Principals of Instrumental Analysis, 5th ed. Suanders, 1998

## Slide 14
HPLC - Resolution
Theoretical Plates (N): The number of theoretical plates characterizes the quality or efficiency of a column.
N = 5.54 [(tR) / w1/2]2 (N = 16 (tR/W)2)
Skoog and Leary: Principals of Instrumental Analysis, 4th ed. Suanders, 1992

## Slide 15
HPLC - Resolution
Theoretical Plates (N): The number of theoretical plates characterizes the quality or efficiency of a column.
N = 5.54 [(tR) / w1/2]2
(N = 16 (tR/W)2)
Plate Height (H): The height equivalent to a theoretical plate (HEPT = H)
H = L / N
Resolution (Rs) depends on the number of theoretical plates:
Rs =
Skoog and Leary: Principals of Instrumental Analysis,
4th ed. Suanders, 1992

## Slide 16
HPLC - Resolution
Capacity Factor (k’): Also called retention factor. Is a measure for the position of a sample peak in the chromatogram.
k’ = (tR1-to)/to
specific for a given compound and constant under constant conditions
A function of column and mobile phase chemistry
Primarily applicable under isocratic conditions
In general, a change in the k’ of one peak will move all peaks in the same direction.
Selectivity Factor (a): Also called separation or selectivity coefficient is defined as
a = k2’/k1’ = (tR2-to) / (tR1-to)
A function of column and mobile phase chemistry
Primarily applicable under isocratic conditions
Changes in selectivity will affect different compounds in different ways.
Skoog and Leary: Principals of Instrumental Analysis, 4th ed. Suanders, 1992

## Slide 17
Capacity Factor
Capacity factor
k´ =
tR - t0
t0
t´R
t 0
=
If the substance is not retained by the stationary phase, e.g. tR = tm, the capacity factor is k' = 0.
Small k' (k < 1) values show that the components are only retained slightly by the separation column. Their peaks are located close to the non-retained peak (k' = 0).
Experience has shown the optimum separation range to be k' values between 1 and 15. Values for k' > 5 mean long retention times with associated band broadening.

## Slide 18
Skoog and Leary: Principals of Instrumental Analysis, 4th ed. Suanders, 1992

## Slide 20: HPLC – Optimizing Separation

## Slide 21: RP-HPLC - Optimization