## Slide 1: Quality Control of Petroleum Product

## Slide 2: Content
Introduction
Classification of laboratory tests
Volatility
Combustion
Viscosity and consistency
Melting point
Oxidation
Corrosion and protection
Miscellaneous tests

## Slide 3: Introduction
Quality control of petroleum products is a necessity if the product are give satisfactory performance to the customer
Each product of specific purpose, standard organization have method of teste and specification

## Slide 4: Classification of laboratory tests
Most of the laboratory tests classified into seven groups –
1.Volatility
Determinant of a hydrocarbon to produce potentially explosive vapours
It is also critically important to an engines start and warm-up

## Slide 5: 2. Combustion
Combustion properties of petroleum products are evaluated by following tests-
Antiknock quality- Octane number, performance number
Ignition quality – Cetane number, Aniline point, Diesel index and cetane index
Calorific value
Burning quality- Smoke point, Char value

## Slide 6: 3. Viscosity and consistency
Determination of viscosity and consistency of petroleum product done by following tests-
Kinematic viscosity :- it is defined as the measure of the resistance to gravity
flow of fluid, the pressure head proportional to density.
Viscosity index:- it is used the effect of change of temperature on the viscosity of any oil.
viscosity index (VI) = 100

## Slide 7: Continue…..
Penetration test:-
determination of the type of bitumen used for a particular application
It used at 25˚C and softening point or penetration at two different temperatures and it can be used to defined the extent to which the consistency of bitumen change with temperature

## Slide 8: 4.Melting point
The test designed to ascertain the tendency of certain petroleum products to melt, liquefy, to solidify, to precipitate wax-like.
Freezing point:- It is the temperature at which crystals of hydrocarbons form on cooling disappear when temperature is rise.
Cloud point :- It is generally determined for product that transparent in a 40 mm thick layer have cloud point below 49 ̊C.
Pour point :- it is the lowest temperature expressed in multiple of 3 ̊C at which the observed to flow when cooled and examined under prescribed
condition.
Drop point of grease :- That temperature at which the thickener is soluble in the base oil that grease become substantially fluid.

## Slide 9: Continue..
Settling point of wax :- The point at which the temperature remains within range of
0.1 ˚ C for 1 min. is taken as the settling point.
Melting point of wax :- it is determined by recording the temperature at which a drop of the sample falls from the bulb of a thermometer when under standard condition.
Softening point of bitumen :- it is as the temperature at which the substance attains a particular degree of softness under specified condition of test.

## Slide 10: 5. Oxidation
Method have been devised for the evaluation of storage stability and resistance to oxidation for gasoline and aviation turbine fuel. These include-
Induction period of gasoline
Thermal stability of jet fuels
Gum content

## Slide 11: 6. Corrosion and protection
Crude oils are corrosive to greater or lesser extent , frequently due to the presence of Sulphur compound , organic acids and traces of brine
Following methods are available –
Total Sulphur
Acidity and alkalinity
Copper-strip corrosion
Silver-strip corrosion test for ATF

## Slide 12: Lecture -2

## Slide 13: CARBON RESIDUE

## Slide 14: CONTENT
-Introduction -Methods -Colour -Density and specfic gravity -Gas chromatography -Refractive index -Wsim -Ductility

## Slide 15
Carbon residue
Carbon residue can be defined as the amount of carbon residue left after evaporation and pyrolysis of oil and is intended to provide some indication of relative coke forming tendency .
Methods
Conradson or Ramsbottom can be used to determine the carbon residue of petroleum products.

## Slide 16
The sample after being weighed into a special glass bulb having a capillary opening is placed in a metal furnace maintained at 550 degree celcius for 20±1 minute. The sample is thus quickly heated to the point. At which all volatile matter is evaporated out of the bulb with or without decomposition while the heavier residue remaining in the bulb undergoes cracking and coking reactions.
Ramsbottom method:-

## Slide 17
Colour colour is an indication of the degree of the products.
Density and specific gravity
Density of a fluid is its mass per unit volume. It is measured over a range of temperature, usually for convince at the temperature at which the fuel is to be stored.
Specific gravity is the ratio of the density of a fluid to that of water at the same temperature. API gravity is an arbitrary figure related to the specific gravity of petroleum products

## Slide 18
Gas Chromatography of Petroleum Gases and Liquids
A measured volume of the sample is introduced itno a chromatography column and transported through the column ,the sample is split into various components, either by adsorption ,depending on the column packing.

## Slide 19
Refractive Index of Hydrocarbon Liquids
Refractive index is defined as the ratio of velocity of light in air to its velocity in the substance under examination. it may also be defined as the sine of the angle of incidence divided by sine of the angle of refraction , as light passes from air in to the substance . The refractive index of liquids varies inversely with both wavelength and temperature. Refractive intercept is calculated by Refractive intercept=n-p/2

## Slide 20
Lead in Gasoline
The lead alkyl s converted to lead chloride and extracted from gasoline by refluxing with concentrated hydrochloric acid. The method covers the gravimetric determination of the total lead content of gasoline and other volatile distillates blended with lead alkyls (tetraethyl lead or tetramethyl lead etc.)

## Slide 21
Water Separation Method
This is carried out with a water separometer. it measure the water separation characteristics of fuels expressed in terms of WSIM. Its measure of fuel cleanliness relative to its freedom from surfactant materials.

## Slide 22
Ductility
Bituminous surfaces exposed to varying temperature conditions undergo a great deal of expansion and contraction . Bitumen having high ductility may be more temperature susceptible.