## Slide 1
Measurement Errors, Precision & Sensitivity
Definitions, formulas and solved numerical examples

## Slide 2
Absolute Error
Absolute error is the difference between the expected value and the measured value of a variable.
e = Yₙ − Xₙ
Yₙ = expected (true) value; Xₙ = measured value
% Error = (e / Yₙ) × 100 = [(Yₙ − Xₙ) / Yₙ] × 100

## Slide 3
Accuracy
Error is frequently expressed in terms of accuracy.
Relative accuracy: A = 1 − |(Yₙ − Xₙ) / Yₙ|
% Accuracy = A × 100%
Also, % Accuracy = 100% − % Error

## Slide 4
Example 1: Error and Accuracy
Expected voltage = 80 V; measured voltage = 79 V.Find absolute error,%error,Relative accuracy and % accuracy
Solution:
Absolute error = 80 − 79 = 1 V
% Error = [(80 − 79) / 80] × 100 = 1.25%
Relative accuracy = 1 − (1/80) = 0.9875
% Accuracy = 98.75%

## Slide 5
Precision
Precision for the nth measurement can be expressed as:
P = 1 − |(Xₙ − X̄) / X̄|
Xₙ = value of nth measurement
X̄ = average value of the set of measurements

## Slide 6
Example 2: Precision of a Measurement
Question: The table gives the set of 10 measurements that were recorded in the laboratory. Calculate the precision of the 6th measurement.
Measurement No. | Measurement value Xₙ
1 | 98
2 | 101
3 | 102
4 | 97
5 | 101
6 | 100
7 | 103
8 | 98
9 | 106
10 | 99
Solution:
X̄ = (98+101+102+97+101+100+103+98+106+99) / 10
X̄ = 1005 / 10 = 100.5
For the 6th measurement: Xₙ = 100
Precision, P = 1 − |(Xₙ − X̄) / X̄|
P = 1 − |(100 − 100.5) / 100.5|
P = 1 − (0.5 / 100.5)
P ≈ 0.995

## Slide 7
Example 3: Load Cell Characteristics
At 20°C: Load (kN) = 0, 0.4, 0.8, 0.12, 0.16, 0.20; Deflection (mm) = 0, 10, 20, 30, 40, 50
At 40°C: Load (kN) = 0, 0.4, 0.8, 0.12, 0.16, 0.20; Deflection (mm) = 3, 14, 25, 36, 47, 58
Determine zero drift, sensitivity drift, sensitivity drift per °C, and resolution.
If 0.5 mm of scale division can be read with fair degree of certainity, then determine the resolution of instrument in both the cases i.e. at 20 degree C and 40 degree C.

## Slide 8
Example 3: Solution – Drift & Sensitivity
Zero drift = 3 mm
Static sensitivity at 20°C = 10 / 0.4 = 25 mm/kN
Static sensitivity at 40°C = 11 / 0.4 = 27.5 mm/kN
Sensitivity drift = 27.5 − 25 = 2.5 mm/kN
Sensitivity drift per °C = 2.5 / 20 = 0.125 (mm/kN)/°C

## Slide 9
Example 3: Resolution
At 20°C: deflection factor = inverse sensitivity = 1/25 = 0.04 kN/mm
For 0.5 mm readable scale division: Resolution = 0.5 × 0.04 = 0.02 kN = 20 N
At 40°C: deflection factor ≈ 1/27.5 ≈ 0.036 kN/mm
Resolution = 0.5 × 0.036 ≈ 0.018 kN = 18 N

## Slide 10
Example 4: Temperature-to-Voltage Transducer
Measurement range: 30°C to 280°C
Output variation: 0 V to 10 V
Determine its sensitivity.
Sensitivity K = (10 − 0) / (280 − 30)
K = 0.04 V/°C = 40 mV/°C