## Slide 1: Methods of Sterilization: In-Bottle Sterilization:
-Milk is filled in the bottle, then it is sterilized
-Milk is pre-heated to 35-40°C.
-Then Clarification, Standardization, Homogenisation, filling, Capping, Sterilization (115°C - 120°C for 15-20mins.), Followed by cooling to room temperature, then storage at room temperature.

## Slide 2: Continuous- flow Sterilization
It is almost same as that of UHT.
But temperature is less than that of UHT and thus requires more time.
Tubular heat exchangers are mostly used for this purpose.

## Slide 3: 2-stage sterilization
Milk is first sterilized using continuous flow method, filled in the bottles, and the bottles are again sterilized, to destory any spores that may enter during bottling procedure.

## Slide 4: Efficiency of Sterilized Milk:
Take 20ml of Milk
Add 4gms of Ammonium Sulphate
Protein will get precipitated due to salt imbalance
Filter it
Filterate Obtained
Heat @ 100°C for 15mins
Turbidity Present (Sterilization not done)