## Slide 1: UNIT –III Thin layer chromatography Introduction, Principle, Methodology, Rf values, advantages, disadvantages and applications
Dr. Nisha Sharma,
Associate Professor
School of Pharmaceutical Sciences
C.S.J.M. University, Kanpur

## Slide 2: THIN LAYER CHROMATOGRAPHY
M. Tsvet- Father of Liq. Chrom. 1900’s
Introduced by Izmailov and Shraiber in 1938- separation of plant extracts
Kirchner: 1950- coated plates- ident. terpenes
E. Stahl in 1958 Designed equipment
Also known as surface, strip, open column, spread layer chromatography

## Slide 3: PRINCIPLE
Based on separation by adsorption
Depends on the relative affinity of components towards stationary and mobile phase
Suppose, affinity of component A has strong towards adsorbent, then the movement will be less. Hence the different constituents separate.
Liquid – solid chromatography

## Slide 4: PRINCIPLE
Competition b/w molecules of analyte & solvent
Both binds with the adsorbent surface
Degree of retention depends upon:
Binding strength of analyte with support
Surface area of support
Amount of mobile phase displaced by the analyte
Binding strength of solvent phase to adsorbent

## Slide 5: PRINCIPLE
The retention may be affected by
Electrostatic interactions
Hydrogen bonding
Dipole dipole interactions
Van der-waals forces

## Slide 6: Methodology
Almost similar to paper chromatography
Coating material:
Adsorbent | Nature | Activity | Mechanism | Substances
Silica gel | Acidic | Active | Adsorption/ Partition | Acidic / neutral
Alumina | Basic | Active | Adsorption/ partition | Basic & neutral
Keisulguhr | Neutral | Inactive | Partition | St. hydrophilic subst
Cellulose powder | Neutral | None | Partition | Water soluble compounds

## Slide 7: Methodology
Coating material: other examples: CaPO4, Mg Trisilicate, silica gel alumina (1:1), acetylated cellulose etc.
Adsorbent : must adhere to plate
Binders: CaSO4, starch, hydrated silica O
Gypsum- widely used binder
Ex: Silica gel G, Alumina G--- G stands for Gypsum
Zinc silicate- inert fluorescent indicator
Ex. Silica Gel GF

## Slide 8: 2. PREPARATION OF TLC PLATES
Suspension of slurry is prepared
Methods to prepare:
Pouring method: back & forth
Dipping: Peifer (1962)- 2 plates at a time- CHCl3 or CHCl3— MeOH
Spraying: Reitsema– Sprayer
Spreading- applicator- aligning tray, spreader, developed by DESAGA (west G)
0.1-0.5 mm thick for analytical work
0.5-2 mm – preparative work
e) Precoated plates- ready to use- 0.1-0.2mm

## Slide 9
3. Activation of Adsorbent: To remove liq. from TLC, Dry for 30min. in air, & then in oven at 110°C fro 30 min, For very active plates- 150°C- 4 hrs
4. Purification of silica gel G layers: To remove Iron as impurity, run plates in MeOH:HCl:: 9:1 v/v, Fe gets migrated to solvent front, again activate at 110°C, but if CaSO4 dissolves reused by adding Suitable binder

## Slide 10
5. Sample application: Microsyringe
Sample solution: non polar/ volatile solvent
6. Developing tank: tank + lid, saturation of tank is must, or lack of reproducibility in Rf
7. Solvent system: Stahl’s triangle: better separation-mix. of solvents
Ex: Ethyl acetate : methanol:: 99:1
Trial error basis – best solvent system

## Slide 11
S
M
E
Eluting solvent
Mixture
Polar
Non polar
Hydrophilic
Lipophilic
inactive
active
Adsorbent activity
Stahl’s triangle

## Slide 12
8. Development methods: Solvent allowed to rise at ht of 15-18cm on 20 cm plate, 20-40 minutes
Solvent front marked and dried
9. Determination of components:
Colorless--- U.V.
Visualizing reagent
Corrosive reagents – chromic acid, H2SO4
10. Evaluation:
Qualitative (R.f)
Quantitative : Direct and indirect methods
Direct: Visual, spot areas, densitometry, direct spectrometry
Indirect: Elution- Instrumental

## Slide 13
After 5 min
After 15 min
a
b
THIN LAYER CHROMATOGRAPHY
sample
Solvent front i.e. distance travelled by solvent
Distance travelled by Sample

## Slide 14: Saturation of TLC Tank
Cover plate
Thin layer plate
Solvent mixture
Solvent wick for saturation

## Slide 15: Advantages
Combines advantages of PC & CC
Equipment simple
Short development time compared to PC & CC
Separation is fairly good on inorganic adsorbent material
Wide choice of stationary phase- adsorption, partition, ion exchange

## Slide 16: Advantages
Fast recovery of separated components – powdery coating of plate, scrapping, spot/ zone, quantitative removal, dissolve, spect./colorimeter
Easy visualization of separated components, florescent compds. Detected easily under U.V. because inorganic background don’t produce fluorescence

## Slide 17: Advantages
Sensitivity: Delineated, sharp spots, 10 to 100 folds as compared to PC
Variable thickness of layers: Thin layers for qualitative and thicker layers for preparative
Chemically inert stationary phase- application of strong heat or corrosive reagent like sulfuric acid
Cost effective

## Slide 18: Disadvantages
Reproducible results are difficult
Not automated procedure
Only non volatile substance or subst. with low volatility can be separated
Length of plate is limited
Separation is in open system- humidity, temp.
Quality of separation is limited

## Slide 19: Applications
Used for separation of all types of natural compounds
To check the purity of samples
As a purification process of isolated compd
To examine the reaction: intermediate products
To identify organic compds.
As a check on process- progress of procedure

## Slide 20: Applications
Used for separation of inorganic ions- cationic, anionic, covalent species. organic deriv. of metals
Sep. of vitamins
Amino acids
Sep. of alcohols, glycols, alkaloids, amines, proteins, antibiotics
Used in all type of Industries, Medicine, Forensic science etc

## Slide 21: References
Jeffry G.H., J. Mendham et al. Vogel’s Text book of Quantitative Chemical Analysis, 5th Edition, 1989, Longman Scientific & Technical, Bath Press, Great Britain.
G.R. Chatwal, SK Anand. Instrumental methods of chemical analysis (Analytical Chemistry), ed. 1995, Himalaya Publishing House, Bombay.
A.H. Beckett & J.B. Stenlake. Practical Pharmaceutcal Chemistry, Part Two, ed. 4th, 1997, (reprint 2003) CBS Publishers & Distributors, New Delhi.