## Slide 1: Er. Mohd. Shah Alam Asst. professor UIET, CSJM University, kanpur

## Slide 2: Advance Computer Networks
            Transport Layer

## Slide 3: Introduction
The transport layer is the fourth layer in the internet model.
Above it is the application layer and below it is the network layer.
This means that transport layer receives services from network layer and provide services to the application layer.
Process to process delivery is achieved through a set of function performed by the transport layer.

## Slide 4: Transport Layer Duties
Packetizing
Connection Control
Addressing
Providing reliability

## Slide 5: Process-to-Process Delivery
The transport layer is responsible for process to Process Delivery.
Addressing
At the transport layer, we need a transport-layer address called Port number, to choose among multiple processes running on the destination host.
In the internet model, the port numbers are
16 –bit integer between 0 and 65,535

## Slide 6: Port numbers
The client program defines itself with a port number, chosen randomly by the transport layer software running on the client host. This is the Ephemeral port number
The internet has decided to use universal port numbers for servers. These are called Well-known port numbers

## Slide 7: IANA Ranges
The IANA (Internet Assigned Number Authority) has divided the port numbers into three ranges..
Well-known Ports: range (0 to 1023)
Registered Ports: range (1024to 49,151)
Dynamic Ports: range (49,152 to 65,535)

## Slide 8: Socket Addresses
Process-to-Process Delivery needs two identifiers, IP address and Port number at each end to make connection.
The Combination of IP address and Port number is called socket address

## Slide 9: Multiplexing and Demultiplexing
Transport layer….

## Slide 10: Connectionless versus Connection-Oriented service
Connectionless service

## Slide 11: Connectionless Service
In a connectionless Service, the packets are sent from one party to another with no need for connection Establishment or Connection release
The packets are not numbered
They may be delayed, lost or arrive out of sequence
There is no Acknowledgement
UDP is connectionless

## Slide 12: Connection-Oriented Service
Connection Establishment:-
Host A sends a packet to announce its wish for connection and includes its initialization information about traffic from A to B.
Host B sends a packet to acknowledge(confirm) the request of A.
Host B sends a packet that includes its initialization information about traffic from B to A.
Host A sends a packet to acknowledge(confirm) the request of B.

## Slide 13: Connection Termination
Host A sends a packet announcing its wish for connection termination.
Host B sends a segment acknowledging the request of A. After this the connection is closed in one direction
When host B has finished sending its own data. It sends a segment to indicate that it wants to close the connection
Host A acknowledge the request of B

## Slide 14: User Datagram Protocol(UDP)
UDP is connectionless, unreliable protocol that has no flow and error control. It uses port numbers to multiplex data from the application layer

## Slide 15: User Datagram
UDP Packets, called user datagram, have a fixed-size header of 8 bytes..
Source port number (16 bits)
Destination port number (16 bits)
Total length (16 bits)
Checksum (16 bits)

## Slide 16: Transmission Control Protocol (TCP)
The reliable, but complex transport-layer protocol. Its add connection-oriented and reliability features to the services of IP.

## Slide 17: Congestion
Congestion in a network may occur if the load on the network(the number of packets sent to the network) is greater than the capacity of the network (the number of packets a network can handle).
Congestion Control refers to the mechanisms and techniques to control the congestion and keep the load below the capacity.

## Slide 18: Congestion Control
Congestion control refers to techniques and mechanism that can either prevent congestion, before it happens, or remove congestion after it happened.
In general we can divide congestion control mechanisms into two broad categories:
Open-loop congestion control (prevention)
Closed-loop congestion control(removal)

## Slide 19: Open-Loop Congestion Control
Policies are applied to prevent congestion before it happens. In these mechanisms, congestion control is handled by either source or destination.

## Slide 20: List of policies that can prevent congestion.
Retransmission policy
Window policy
Acknowledgement policy
Discarding policy
Admission policy

## Slide 21: Closed-loop congestion control
Back pressure
Choke point
Implicit signaling
Explicit signaling
Backward signaling
Forward signaling