## Slide 1: PASTEURIZATION
PASTEURIZERS:
Batch
HTST
Vat
Vacuum
BATCH PASTEURIZATION:
For this, double jacketed vat is used.
This is also known as LTLT (Low-Temperature-Long-Time) pasteurization.
Time-Temperature combination required is - 63°C for 30 minutes.
After heating promptly cooled to 5°C or below.
In this ,there are mainly 3 types of pasteurizers:
a) Water- jacketed vat:
This is double-walled jacket in sides and bottom in which hot water or steam are circulates for heating
b. Water spray type:
A film of water is sprayed from a perforated pipe over the surface of tank which is holding the product.
c. Coil- vat type:
In this the heating or cooling medium is pumped through coil which is either in horizontal or vertical position.
Coil is turned through the product. The turning coil agitates the product.

## Slide 2: HIGH TEMPERATURE SHORT TIME:
This is modern method of pasteurizing milk.
It gives a continuous flow of milk.
Milk is heated at 71.5°C for 15 seconds.
Plate heat exchanger are used for this process.
Raw milk is moves from storage tank to float control balance tank, used to control the flow rate of milk.
Homogenisation and clarification of milk are done before pasteurization of milk.
Plates of plate heat exchanger are 1.5 to 3mm in thickness.
They are used for all heating, cooling, regeneration and holding process.
The distance between 2 plates is of 3-5 mm and these plates are pressed.
Each of these plates have corrugation to provide turbulent flow to the milk.
After passing through plate, milk comes to the flow diversion valve.
This is based on air pressure.
Raw milk will enter into regeneration section from where it moves to the pasteurization section with the holding time of - 15 seconds. It moves to regeneration cooling section followed by cooling.
Time taken from the end of heating to FDV is the holding time.
Note:- Holding time is defined as the flow time of fastest particles of milk at prescribed temperature through the holding section.

## Slide 3: VACUUM PASTEURIZATION:
In this pasteurization of milk is done under reduced pressure.
Direct steam is used.
The vacreator consists of 3 stainless steel chambers which is connected to one another for steam heating and vacuum treatment with continuous product flow.
STASSANIZATION:
This method is carried out in a tubular heat exchanger consisting of three concentric tubes.
The milk is heated at 74°C for 7 seconds.
ULTRA HIGH TEMPERATURE:
Time-Temperature combination of UHT is - 135°C-150°C for no-holds or fraction of second.
Efficiency of UHT heat treatment of milk depends on immidiate aseptic packing.

## Slide 4: Advantages of HTST pasteurization:
Capacity of heat- treat milk quickly.
Less floor space required.
Lower initial cost.
Reduced milk loss.
Development of thermophiles not a problem.
DISADVANTAGES:
Complete drainage is not possible.
The system is not well- adapted to handling small quantities of several liquid milk products.
Greater accumulation of milk-stone in the heating section.
Skilled manpower is needed.