## Slide 1: House keeping -4
Dr Versha Prasad

## Slide 2: Cleaning Agents and Disinfectants
Cleaning is the removal of foreign material (e.g., dust, soil, organic material such as blood, secretions, excretions and microorganisms) from a surface or object.
Cleaning physically removes rather than kills microorganisms, reducing the organism load on a surface. It is accomplished with water, detergents and mechanical action. The key to cleaning is the use of friction to remove microorganisms and debris.
Thorough cleaning is required for any equipment/device to be disinfected, as organic material may inactivate a disinfectant.
This may be accomplished through a two-step process involving a cleaner followed by a disinfectant, but is more commonly accomplished in the health care organisation through a one-step process using a combined cleaner/disinfector product.

## Slide 3: Cleaning Agents and Disinfectants
Disinfection is a process used on inanimate objects and surfaces to kill microorganisms.
Disinfection will kill most disease-causing microorganisms but may not kill all bacterial
spores. Only sterilization will kill all forms of microbial life.

## Slide 4
Detergents remove organic material and suspend grease or oil.
Equipment and surfaces in the health care setting must be cleaned with approved hospital-grade cleaners and disinfectants.
Equipment cleaning/disinfection should be done as soon as possible after items have been used.
A variety of products from a number of suppliers can be used to achieve effective cleaning. It is important to follow the manufacturer’s instructions when using cleaning agents.

## Slide 5: Hospital-grade disinfectants
Hospital-grade disinfectants for use in all health care settings include:
 Alcohols
o 60-90% ethyl or isopropyl alcohol
 Chlorine
o Sodium hypochlorite (‘bleach’)
o Calcium hypochlorite
 Phenolics
 Quaternary Ammonium Compounds (‘QUATs’)
 Iodophors
 Hydrogen Peroxides (1

## Slide 6: Alcohols (70-95%)
External surfaces of some equipment (e.g., stethoscopes)
 Noncritical equipment used for home health care
 Disinfection is achieved after 10 minutes of contact.
 Observe fire code restrictions for storage of alcohol.
Advantages
Non-toxic
Low cost
Rapid action
Non-staining
No residue
Effective on clean equipment/devices that can be immersed

## Slide 7: Chlorines (e.g., sodium hypochlorite or bleach)
Hydrotherapy tanks, exterior surfaces of dialysis equipment, cardiopulmonary training mannequin, environmental surfaces (use 0.1% for surfacecleaning and soaking of items)
 Noncritical equipment used for home health care
 Blood spills (use 0.05% sodium hypochlorite for a minor blood spill and 0.5% for a major blood spill)
Advantages
Low cost
Rapid action
Readily available in non hospital settings
Sporicidal at higher Concentration

## Slide 8: Phenolics
Floors, walls and furnishings
 Hard surfaces and equipment that do not touch mucous membranes (e.g., IV poles, wheelchairs, beds, call bells)
 DO NOT use phenolics in nurseries
Advantages
Leaves residual film on environmental surfaces
Commercially available with added detergents to provide one-step cleaning and disinfecting
Slightly broader spectrum of activity

## Slide 9: Quaternary ammonium compounds (QUATs)
Floors, walls and furnishings
Blood spills prior to disinfection
Advantages
Non-corrosive, nontoxic, low irritant
Good cleaning ability, usually have detergent
May be used on food surfaces

## Slide 10: Iodophors (Non-antiseptic formulations)
Hydrotherapy tanks
Thermometers
Hard surfaces and equipment that do not touch mucous membranes (e.g., IVstands, wheelchairs, beds, call bells)
DO NOT use antiseptic iodophors as hard surface disinfectants
Advantages
Rapid action
Non-toxic

## Slide 11: Hydrogen peroxide enhanced action formulation (HPEAF) 0.5% (7% solution diluted 1:16
Isolation room surfaces room surfaces
Low-level disinfection is achieved after 5 minutes of contact at 20°C.
Monitoring not required, however test kits are available from the manufacturer
Advantages
Safe for environment
Non-toxic
Rapid action
Available in a wipe
Active in the presence of organic material
Excellent cleaning

## Slide 12: General principles while using a hospital disinfectant:
 It is most important that an item or surface be free from visible soil and other items that might interfere with the action of the disinfectant, such as adhesive products, before a disinfectant is applied, or the disinfectant will not work.
 A hospital-grade disinfectant may be used for equipment that only touches intact
skin.
 It is important that the disinfectant be used according to the manufacturer’s
instructions for dilution and contact time.

## Slide 13: General principles while using a hospital disinfectant:
Minimize the contamination levels of the disinfectant solution and equipment used for cleaning.
This can be achieved by ensuring proper dilution of the disinfectant, frequently changing the disinfectant solution and by not dipping a soiled cloth into the disinfectant solution (i.e., no ‘double-dipping’).
Personal protective equipment must be worn appropriate to the product(s) used.
There should be a quality monitoring system in place to ensure the efficacy of the disinfectant over time (e.g., frequent testing of product).