## Slide 1: TABLET (UNIT -2)
Mrs Kalpana
(Assistant Professor)
U.I.O.P, CSJMU
Kanpur-208019
PART -I

## Slide 2: Tablet Additives
In tablet other than active ingredients it also contains a number of inert materials known as excipients or additives. Different excipients are:
Diluent
Binder or adhesive
Disintegrents Main components of
Tablet
Lubricants and glidants
Coloring agents
Flavoring agents
Sweetening agents

## Slide 3: Diluents
When the drug dosage itself is inadequate to produce the bulk than Diluents or fillers are used to make required bulk of the tablet
Diluents also provide better tablet properties such as to permit the use of direct compression manufacturing process , improve cohesion and to promote flow.
A diluents should have following properties:
They must be non toxic
They must be commercially available in acceptable grade.
There cost must be low

## Slide 4
They must be physiologically inert .
They must be physically & chemically stable by themselves & with the drugs.
They must be free from all microbial contamination.. They do not alter the bioavailability of drug.
They must be color compatible.
Eg: Commonly used tablet diluents
Lactose-anhydrous
Spray dried lactose
Directly compressed starch-Sta Rx 1500
Hydrolyzed starch-Emdex &Celutab
Microcrystalline cellulose-Avicel (PH 101and PH 102)
Dibasic calcium phosphate dehydrate
Calcium sulphate dihydrate
Mannitol
Sorbitol
Sucrose- Sugartab, DiPac, Nutab 10. Dextrose

## Slide 5: Binders and Adhesives
These materials are used either in dry or wet- form to form granules or to form cohesive compacts for directly compressed tablet.
Example :
Acacia, tragacanth- Solution for 10-25% Conc.
Cellulose derivatives- Methyl cellulose, HPC, HPMC
Gelatin- 10-20% solution
Glucose- 50% solution
Polyvinylpyrrolidone (PVP)- 2% conc.
Starch paste-10-20% solution
Sodium alginate

## Slide 6: Disintegrants
Disintegrants are added to a tablet formulation to facilitate the breaking or disintegration of tablet or granules, when it comes in contact with water of GIT.
Example
Starch- 5-20% of tablet weight.
Starch derivative – Primogel and Explotab (1-8%)
Clays- Veegum HV, bentonite 10% level in colored tablet only
Cellulose derivatives- Ac- Di-Sol (sodium carboxy methyl cellulose)
Alginate
PVP (Polyvinylpyrrolidone), cross-linked

## Slide 7: Superdisintegrants
Superdisintegrants in tablet swells up to ten fold within 30 seconds as comes in contact of water.
Example : Crosscarmellose- cross-linked cellulose, Crosspovidone- cross-linked povidone Sodium starch glycolate- cross-linked starch.
These cross-linked products swell upto 10 fold with in 30 seconds as comes in contact of water
stages of addition :A part of disintegrant is added before granulation and a part before compression, which serve as glidants or lubricant.
Evaluation of carbon dioxide in effervescent tablets is also one way of disintegration

## Slide 8: Lubricant and Glidants
To prevent adhesion of the tablet materials to the surface of dies and punches lubricant is used.
Glidants are used to promote flow of powder or granules material by reducing the friction between the particles.
Example:
Lubricants-, Stearic acid salt - Stearic acid, Stearic acid, Talc, Magnesium stearate,PEG (Polyethylene glycols), Surfactants
Glidants-Silica derivative - Colloidal silica
Corn Starch – 5-10% conc., Talc-5% conc.,

## Slide 9: Coloring agent
The use of colors and dyes in a tablet has three purposes
Product Identification
Masking of off color drugs
Production of more elegant product
All coloring agents must be approved and certified by FDA. Two forms of colors are used in tablet preparation – FD &C and D & C dyes. These dyes are applied as solution in the granulating agent or Lake form of these dyes. Lakes are dyes absorbed on hydrous oxide and employed as dry powder coloring.
Example: FD & C yellow 6-sunset yellow ,FD & C yellow 5- Tartrazine , FD & C green 3- Fast Green ,FD & C blue 1- Brilliant Blue ,FD & C blue 2 - Indigo carmine D & C red 3- Erythrosine., D & C red 22 – Eosin Y

## Slide 10
Flavoring agents:
For chewable tablet- oil flavours are used
Sweetening agents
For chewable tablets: Sugar, mannitol. Saccharine (artificial): 500 time’s sweeter than sucrose
Disadvantage: Bitter aftertaste and carcinogenic
Aspartame (artificial)
Disadvantage: Lack of stability in presence of moisture.