## Slide 1: PN JUNCTION (ESC-S101) (Atul Kr. Agnihotri )

## Slide 2: P-N Junction
We create a p-n junction by joining together two pieces of semiconductor, one doped n-type, the other p-type.

## Slide 3: P-N Junction
In the n-type region there are extra electrons and in the p-type region, there are holes from the acceptor impurities .

## Slide 4: P-N Junction
In the p-type region there are holes from the acceptor impurities and in the n-type region there are extra electrons.

## Slide 5: P-N Junction
When a p-n junction is formed, some of the electrons from the n-region which have reached the conduction band are free to diffuse across the junction and combine with holes.

## Slide 6: P-N Junction
Filling a hole makes a negative ion and leaves behind a positive ion on the n-side.
A space charge builds up, creating a depletion region.

## Slide 7: P-N Junction
This causes a depletion zone to form around the junction (the join) between the two materials.
This zone controls the behavior of the diode.

## Slide 8: Forward Biasing
Forward biasing the p-n junction drives holes to the junction from the p-type material and electrons to the junction from the n-type material.

## Slide 9: Forward Biasing
At the junction the electrons and holes combine so that a continuous current can be maintained.

## Slide 10: Diode
A diode is the simplest possible semiconductor device.

## Slide 11: One Way Electric “Turnstile”
A diode allows current to flow in one direction but not the other.

## Slide 12: Reverse Biasing
The application of a reverse voltage to the p-n junction will cause a transient current to flow as both electrons and holes are pulled away from the junction.

## Slide 13: Reverse Biasing
When the potential formed by the widened depletion layer equals the applied voltage, the current will cease except for the small thermal current.

## Slide 14
This voltage is needed to start the hole-electron combination process at the junction.
When forward-biased, there is a small amount of voltage necessary to get the diode going. In silicon, this voltage is about 0.7 volts.

## Slide 15: Diode Characteristic
When reverse-biased, an ideal diode would block all current. A real diode lets perhaps 10 microamps through -- not a lot, but still not perfect.

## Slide 16: Diode Characteristic
Usually, the breakdown voltage is a lot more voltage than the circuit will ever see, so it is irrelevant.