## Slide 1: Acceleration analysis

## Slide 2: Velocity analysis
Problem-1: PQRS is a four bar chain with link PS fixed. The lengths of the links are PQ = 62.5 mm ; QR = 175 mm ; RS = 112.5 mm and PS = 200 mm. The crank PQ rotates at 10 rad/s clockwise. Draw the velocity and acceleration diagram when angle QPS = 600 and Q and R lie on the same side of PS. Find the angular velocity and angular acceleration of links QR and RS.
Step -1: Draw Configuration Diagram with suitable scale
Step -2: Draw Velocity diagram
Define scale: 200 mm = 4 inch
 | Actual length | Drawing dimension
Link PQ | 62.5 mm | 1.25 inch
Link QR | 175 mm | 3.5 inch
Link RS | 112.5 mm | 2.25 inch
Link PS | 200 mm | 4 inch
Fixed
Link
P
S
200 mm ( 4 inch)
600
62.5 mm ( 1.25 inch)
Q
R
175mm ( 3.5 inch)
112.5 mm
( 2.25 inch)
Configuration Diagram
ωPQ = 10 rad/s clockwise
VQ = ωPQ x PQ
= 10 x 0.0625 m
= 0.625 m/s
VQ ⊥ PQ
Define scale : 0.625 m/s = 2.5 inch
P
S
600
Q
R
VQ
ωPQ = 10 rad/s
900

## Slide 3: Velocity analysis
Step -2: Draw Velocity diagram
VQ = 0.625 m/s
VQ ⊥ PQ
Define scale : 0.625 m/s = 2.5 inch
VR ⊥ RS
VR/Q ⊥ QR
P
S
600
Q
R
VQ
ωPQ = 10 rad/s
900
VQ
VQ
2.5 inch
VQ
p , s
q
900
Direction of velocity of R
Locus of r
Perpendicular to QR.
Direction of velocity
Of R with respect to Q.
r
Velocity diagram

## Slide 4: Velocity analysis
VQ/P
p , s
q
r
Velocity diagram
VR/Q
VR/S
R= 1.3 inch
pq | 2.5 inch | 0.625 m/s
qr | 1.3inch | 0.325 m/s
pr | 1.66 inch | 0.415 m/s
0.625 m/s = 2.5 inch
ωQR | Angular speed of link QR
ωRS | Angular speed of link RS
 | Actual length | Drawing dimension
Link PQ | 62.5 mm | 1.25 inch
Link QR | 175 mm | 3.5 inch
Link RS | 112.5 mm | 2.25 inch
Link PS | 200 mm | 4 inch
ωQR = 1.86 rad/s
ωRS = 3.69 rad/s
Need for acceleration diagram

## Slide 5: Velocity analysis
VQ/P
p , s
q
r
Velocity diagram
VR/Q
VR/S
pq | 2.5 inch | 0.625 m/s
qr | 1.3inch | 0.325 m/s
pr | 1.66 inch | 0.415 m/s
0.625 m/s = 2.5 inch
ωQR | Angular speed of link QR
ωRS | Angular speed of link RS
 | Actual length | Drawing dimension
Link PQ | 62.5 mm | 1.25 inch
Link QR | 175 mm | 3.5 inch
Link RS | 112.5 mm | 2.25 inch
Link PS | 200 mm | 4 inch
ωQR = 1.86 rad/s
ωRS = 3.69 rad/s
Need for acceleration diagram

## Slide 6: Acceleration analysis
P
S
600
Q
R
aQ
aR/Qr
aR/Qr = radial component of acceleration of R with respect to
Q acting along RQ direction.
aR/Qt
aR/Qt = tangential component of acceleration of R with respect to Q
acting perpendicular to RQ direction.
aR/Q = aR/Qr + aR/Qt
aR/Qr
aR/Qt
aR/Qr
aR/Qt
aR/Q
aQ
aR/Qr
aR/Qt
Angular acceleration of link RQ
Not Known
m/s2
ωQR = 1.86 rad/s
Get through velocity
Diagram.
m/s2
m/s2
m/s2
Define scale:
6.25 m/s2 = 1.5 inch
0.605 m/s2 = 0.145 inch
aQ
aR/Qr
aR/Qr

## Slide 7: Acceleration analysis
P
S
600
Q
R
aQ
aR/Qr
aR/Qt
aQ
aR/Qr
aR/Qt
Angular acceleration of link RQ
Not Known
m/s2
ωQR = 1.86 rad/s
Get through velocity
Diagram.
m/s2
m/s2
m/s2
Define scale:
6.25 m/s2 = 1.5 inch
0.605 m/s2 = 0.145 inch
aQ
aR/Qr
aQ
aR/Qr
aR/Qt
Locus of r

## Slide 8: Acceleration analysis
P
S
600
Q
R
aQ
aQ
aR/Qr
aR/Qt
Locus of r
aR/Sr
aR/St
900
aR/Sr
aR/St
Angular acceleration of link RS
Not known to us
Define scale:
6.25 m/s2 = 1.5 inch
1.52 m/s2 = 0.365 inch
aR/Sr
Locus of r
(p , s)
q
r1
r
r2
aR/St
(p , s)
q
r1
r
r2
Acceleration diagram
aR/Sr
aR/St
aQ
aR/Qr
aR/Qt
aR/Qt
RQ
aR/St
aR/St
RS