## Slide 1: Solid Modeling
Solid Modeling is the computer modeling of 3D solid objects. The objective of Solid Modeling is to ensure that every surface is geometrically correct.
It is considered the most complex aspect to master in computer-aided design (CAD) because it requires the CAD software to simulate the object from within and outside.
This is critical as it lets designers provide cutaways of the design, such as an engine and its components. In short, solid modeling allows the design, creation, visualization and animation of digital 3D models.
Representing Solids
Based on assumed mathematical properties, any scheme of representing solids is a method for
capturing information about the class of semi-analytic subsets of Euclidean space. This
means all representations are different ways of organizing the same geometric and
topological data in the form of a data structure. All representation schemes are organized in
terms of a finite number of operations on a set of primitives. Therefore, the modeling space of
any particular representation is finite, and any single representation scheme may not
completely suffice to represent all types of solids. For example, solids defined via
combinations of regularized boolean operations cannot necessarily be represented as the
sweep of a primitive moving according to a space trajectory, except in very simple cases.
This forces modern geometric modeling systems to maintain several representation schemes
of solids and also facilitate efficient conversion between representation schemes

## Slide 2: Primitive Instancing
This scheme is based on notion of families of object, each member of a family
distinguishable from the other by a few parameters. Each object family is called a generic
primitive, and individual objects within a family are called primitive instances. For example,
a family of bolts is a generic primitive, and a single bolt specified by a particular set of
parameters is a primitive instance. The distinguishing characteristic of pure parameterized
instancing schemes is the lack of means for combining instances to create new structures
which represent new and more complex objects. The other main drawback of this scheme is
the difficulty of writing algorithms for computing properties of represented solids. A
considerable amount of family-specific information must be built into the algorithms and
therefore each generic primitive must be treated as a special case, allowing no uniform
overall treatment.

## Slide 3: Boundary Representation
Boundary Representation, or B-rep for short, can be considered as an extension to the
wireframe model. The merit of a B-rep is that a solid is bounded by its surface and has
its interior and exterior. The surface of a solid consists of a set of well-organized faces, each
of which is a piece of some surface (.e.g., a surface patch). Faces may share vertices and
edges that are curve segments. Therefore, a B-rep is an extension to the wireframe model by
adding face information to the latter.
There are two types of information in a Brep: topological and geometric. Topological information provides the relationships among
vertices, edges and faces similar to that used in a wireframe model. In addition to
connectivity, topological information also includes orientation of edges and
faces. Geometric information is usually equations of the edges and faces.
The orientation of each face is important. Normally, a face is surrounded by a set of vertices.
Using the right-handed rule, the ordering of these vertices for describing a particular face
must guarantee that the normal vector of that face is pointing to the exterior of the solid.
Normally, the order is counter clockwise. If that face is given by an equation, the equation
must be rewritten so that the normal vector at every point on the part that is being used as a
face points to the exterior of the solid. Therefore, by inspecting normal vectors one can
immediately tell the inside and outside of a solid under B-rep