## Slide 1: 7th Semester, Pharm. Quality Assurance
Unit IV
Complaints: Complaints & Evaluation Of Complaints, Handling Of Return Good, Recalling & Waste Disposal
Dr Nisha Sharma

## Slide 2: INTRODUCTION: COMPLAINTS
Definition: A statement that says something is unsatisfactory or unacceptable about the product/ packaging in terms of any defect in Pharmaceutical product
May be received from Pharmacists, Physicians, wholesalers, Retailers, Patients.
Therefore, as per GMP, Industry has their own procedures to maintain records, investigation and review steps of complaints & accordingly a system to recall the product from the market.

## Slide 3
Types of complaints
TYPE A Critical
TYPE B Major
TYPE C Minor
Adverse drug reactions
Major health issues
Safety & purity
Product Stability issues
Potency of product
Issues related to foreign matter in product/ mix ups
Changes in Chemical/ Physical properties
Problem in primary packaging
Issues related to labeling or coding of batch details
Secondary packaging material problems etc

## Slide 4
Types of complaints
Quality Complaints
Adverse Reaction complaints
Other medical related
Physical/ chemical / biological properties related
Labeling or packaging
Allergic reactions
untoward reaction
fatal reaction from product
lack of efficacy
Therapeutic response of product

## Slide 5: VARIOUS COMPLAINTS
Physical properties | Colour, smell or taste of products | possible deterioration of products
Product | • Less products found container • Contamination with toxic substances and microbial spoilage Adverse reaction after consuming product | possible leaking or production issues contamination issues presence of possible allergens or prohibited substances
Packaging | •Wrong label, missing label, wrong products, leakage •Damage of packing | possible mix up and contamination
Delivery | Slow delivery or products were wet when it was received | delivery issues

## Slide 6: SOURCES OF COMPLAINTS
SOURCES OF COMPLAINTS
Internal
External
Verbal
Written
Complaint from Production, Quality Control, Warehouse, Sales Department
From customers, doctors, paramedics, clinics, hospitals, drugstores,
received by oral means & must be documented by authorized person
Received in writing like mail, letter etc.

## Slide 7: EVALUATION OR INVESTIGATING NG THE COMPLAINTS
STEPS IN RESOLVING THE PRODUCT COMPLAINTS OR INVESTIGATION OR EVALUATION
STEPS
1. Receiving
2. Investigating
3. Root Analysis of cause
4. Handling
5. Recording

## Slide 8: 1. Receiving the complaints
CUSTOMER
Company Contact person
Quality assurance Complaint officer
Complaint thru email/ toll free number etc.
Open the investigation form that includes customer personal details like name, address etc. & information about the complaint related to product ex. Batch no., lot no., product name, Mfg. & expiry date etc.
Maintain complete documentation
Decide the proper remedy
Interdisciplinary teams required
Record the complaint: product detail, type of defect, testing retention samples, review of batch production, distribution records etc

## Slide 9: 2. Technical Investigation
START INVESTIGATION
Documentation based Investigation
Previous complaints of same type with same batch
Reporting of non conformation in batch records
Laboratory based Investigation
Comparison of Complaint and retained sample
Results reported to QA complaint Officer
QA complaint officer QACO
QA CO prepares final report or conclusion
Checks the seriousness of complaint & unexpected adverse drug issues
Reports the concerned health authorities
CONFIRMED COMPLAINTS
If complaint & retained samples show out of specification (OOS)
Only complaint sample is OOS & is single failing product
NON CONFIRMED COMPLAINTS
When complaint & retained sample are in compliance with specification
Complaint sample is OOS due to misuse/ mishandling
COUNTERFEIT OR TAMPERED SUSPICIOUS COMPLAINTS
Only complaint sample is OOS
No definite reason , like packaging material is different
Legal affairs to be informed for further actions

## Slide 10: 3. CORRECTIVE ACTIONS AND FEEDBACK TO CUSTOMERS
After Investigation by
QA COMPLAINT OFFICER
Corrective action
Depends on nature of complaint
Range from quick trainings to formal CAPA (corrective action & preventive action)
Check if quality problem is with specific lot or others , consider possibility of Recall
Feedback to the customer
Write a letter to customer about the investigative approach taken, results found, their implications
Deliver a free offer product to reimburse the customer (if required)

## Slide 11: 4. MONTHLY REPORT & TREND ANALYSIS BY QA OFFICER
QA Complaint officer should
elaborate monthly reports containing : How many complaints did the company received in the period, how many confirmed complaints, non confirmed, or counterfeit , which products did not receive major number of complaints, what is nature of these complaints, which batched are involved, what were the root cause of confirmed complaints, How much the complaint handling cost to company
Pareto analysis a good statistical tool to identify main confirmed complaints that has to be treated first
Deliver the report to QA, QC, Production management, Marketing, Finance, Human resources, Regulatory and Legal Affairs

## Slide 12: RECORDING OF COMPLAINTS
Records Of Complaints Include
Contents of complaint
Name, dosage form, type of package, batch no., date, place of complaint, cause of complaint, name & address of complainant
Result of investigations
Condition in which defect observed, result of investigation, reference sample type, its analysis
Follow up measures
Reply to complainant
Remedial action taken, informing serious defects that may arise in future to competent authorities

## Slide 13: HANDLING OF RETURNED GOODS/PRODUCTS
Bulk/ finished product when sent back to Manufacturer, distributor, importer is known as returned goods
Reasons for Return of goods may be because of any complaint, damage, product expiry, or other reasons
Salvaged drug products: are returned goods which had been subjected to improper storage conditions like extreme temp., humidity, smoke, fumes, pressure, radiation
Classification of returned Goods
Goods that can be reprocessed to comply with appropriate specifications
Unacceptable drug product
Goods that still comply with all acceptable standards according to investigation by QC dept

## Slide 14: HANDLING OF RETURNED GOODS
Approved written procedures for holding, testing, reprocessing of returned products to be followed
Records of such products be maintained, name, label potency, lot/batch no., reason of return, quantity returned, date of disposition, ultimate disposition
Proper identification & placed under quarantine
Should be destroyed if quality is unsatisfactory- packaging, labeling, container, carton etc creates doubt about safety, identity, strength, quality, or purity
After critical assessment the QC of goods like testing for purity, strength, identity, safety, etc may be taken for resale or relabeling. Actions should be recorded in writing.
Reprocessing of goods can be done if after reprocessing if leads to a standard product
If it looks that the returned products involve some related batches also then such reference sample from such batches shall be investigated

## Slide 15: Recalling of Products
Recalling means withdrawing or removing the product from distribution network as of quality issues/ adverse drug reactions
Recall can be done by Manufacturer or distributor
TYPES OF RECALL
Class I
Probability that product may cause serious adverse health issues/ death
Class II
Product may cause temporary Adverse health issues or serious adverse health issues are remote
Class III
Product may not cause any adverse health consequences

## Slide 16: STAGES OF PRODUCT RECALL
I STAGE: Receipt of Product complaint
Recall may be done against Complaint received by company or as a result of analysis done in the Production unit itself.
Serious adverse reactions of class I & II must be reported to Health authorities with in 24 hrs after receipt of complaint.
Less serious ones of class III must be reported with in 72 hours to the Health authorities
II STAGE: Initiation of product recall
Immediately after the decision on recall of product is final, the company should notify on a Recall Notification Form to the Government Health Authority about recall. Information in Form consist of :
Details of Product: Name, name of API, dosage form, strength, MFG License no., pack size, batch no., Mfg. & expiry dates, date of product release/ import. Contact details of Manufacturer/ distributors
Details of the Problem: Name, Tel. no. of person reporting problem, date of report, physical location of problem, nature of problem, no. of similar report received, results of test, other investigation on suspect or similar samples.
Health Hazard evaluation and proposed action: Type of hazard, its evaluation, proposed recall classification, level, availability of alternative products

## Slide 17: STAGES OF PRODUCT RECALL
III STAGE: RECALL STRATEGY
Depending upon nature of deficiency in product, incidence of complaints, public safety, distribution networks, recovery procedures, resources for corrective action, availability of alternative products recall strategy is framed
LEVELS OF RECALL:
WHOLESALE LEVEL RECALL
Recalling of product is done from all parties involved in wholesale distribution of product & include wholesalers and retailer
B) RETAIL LEVEL RECALL
From all public & private hospital pharmacies, retail pharmacies, clinical investigators, institutions involved in clinical investigations, medical, dental, healthcare practitioners, nursing homes, medical shops, health food stores etc.
CONSUMER LEVEL RECALL
Includes patient and other consumers

## Slide 18: STAGES OF PRODUCT RECALL
IV STAGE: PUBLIC ALERT
For Class I and Class II hazards, rapid alert is issued to public. The alert may be issued through press release, media etc.
V STAGE: EVALUATION OF RECALL
It is responsibility of Mfg. to ensure effective recalling, which is examined by Govt. Health authorities. If found that the recalling is not effective, recall letters are issued again by Govt. to the Mfg.
After complete recall, the Mfg. has to submit complete data of Recalled products to Govt. Health authorities, along with remedial measures proposed to prevent such reoccurrence in future

## Slide 19: Waste Disposal
Waste: Term by Environmental Protection Act 1990.
Waste: includes any effluent, unwanted surplus substances which requires disposal as it is worn out, contaminated or spoiled. They are not in the chain of commercial utility
Called as Surplus material: if qty is more than required
Obsolete: If no longer usable
Obsolescence : If no longer required but can be used
Types of Waste:
1. Biodegradable : Paper, wood, fruits, Pharmaceutical, biomedical etc.
2. Non Biodegradable : Plastics, oil machines, cans etc.
OR
Hazardous waste: Unsafe for use
Non Hazardous waste: safe to use

## Slide 20: GENERATION OF PHARMACEUTICAL PRODUCT WASTE
Waste generation during weighing, filtering, milling, transferring
Waste extracted during dust extraction system while Mfg
During compression, coating, filling, packaging etc
During in process checks like weight variation, volume checks etc.
From printed packaging materials like labels, leaflets, cartons, foils in packaging process
Expired products, damaged products returned back
Excess samples with QC dept. after their tests
All are required to collected, accounted and disposed off as per established procedures and guidelines.

## Slide 21: Different Legislations in India for Waste
1. The Air (Prevention & control of pollution) Act, 1981
2. The Air (Prevention & control of pollution) Rules, 1982
3. The Water (Prevention & control of pollution) Act, 1974
4. The Water (Prevention & control of pollution) Rules, 1975
5. The Environment Protection Act and Rules, 1977
6. Hazardous waste Management & Handling Rules, 1989
7. Bio Medical Waste Management & Handling Rules, 1998
Some Ingredients of Pharmaceutical waste | Limit permitted
Oil & Grease | 10 mg/l
Mercury | 0.01 mg/l
Lead | 0.10 mg/l
Phenolic | 1 mg/l
Chromium | 0.1 mg/l
Arsenic | 0.2 mg/l

## Slide 22: METHODS OF WASTE DISPOSAL
Return to Manufacturer: The unused drugs with disposal problems like Anti-cancer or which have nearby expiry are returned
Landfill: For solid waste, old method to place waste directly to land. 03 types of lanfills are:
Open uncontrolled non engineered dump landfill: Untreated waste is dumped. Harms environment. Not used now
Engineered landfill: dump landfill is with features to protect environment
Highly Engineered sanitary landfill: constructed & operated landfill sites offering safe route of pharmaceutical waste disposal
3. Waste immobilization (encapsulation): Immobilization of waste in plastic or steel drums is done before disposing. Cleaning of drums later must be done adequately to prevent traces of materials
4. Waste inertization : Remove Packaging materials → Remove dosage forms ex. Blister pack→ Add water+cement+lime →Grind → homogenous paste → transport to landfill

## Slide 23: METHODS OF WASTE DISPOSAL
5. Sewer: For large qty’s of Liquid dosage forms: Syrups, IV fluids, dilute with water → Flush in small qty’s over a period of time
For Small qty’s after dilution can be flushed by fast flowing water
6. Medium temperature incineration: High Temp. incinerator are used for more than 1% halogenated compounds
Medium temperature furnaces operating at min. 850°C used to treat expired solid dosage forms
STEPS TO DISPOSE OFF WASTE:
Handling of pharmaceutical waste: Responsibility of Production employees, Quality assurance personel. How to handle & final disposal to avoid misuse or accidents?
Treatments of Pharmaceutical waste: Written procedures for disposal. Collection of waste in closed containers → label → place at secure separate place till destroyed
Done by authorized person, with precautions to protect environment.

## Slide 24: Method To Dispose Pharmaceutical Waste
No. | Type of Waste | Method
1 | Empty containers of bulky materials | Empty the containers, rinse with water, remove labels, dispose
2. | Powders, granules, tablets, capsules | Make solution in water or suitable solvent, pour solution to effluent treatment plant
3 | Oral & parental prep. | Pour in effluent treatment plant
4 | Strips/ blister packs | Recover tabs/capsules by de -foiling , destroy tablets/ capsules as per SOP
5 | Labeled bottles | Remove labels, destroy bottles by crushing them
6 | Printed labels, cartons, foils, leaflets | Destroy by incineration

## Slide 25: Method To Dispose Pharmaceutical Waste By Category
No. | Type of Waste | Method
1 | Solids | Landfill
2. | Semi Solids | Encapsulation
3 | Powders | Medium & high temperature incineration
4 | Liquids | Sewer
5 | Ampoules | Crush and flush to sewer
6 | Anti-infective drugs | Encapsulation
7 | Antineoplastics drugs | Return to Mfg/ encapsulation/ medium & high temp. incineration
8 | Aerosol canisters | Landfill
9 | Disinfectants | Sewer
10 | PVC Plastic, glass | Landfill
11 | Paper, cardboard | Recycle, LANDFILL

## Slide 26: Methods of Disposal In Emergencies
Types Of Pharmaceutical Dosage Forms | Methods
Solids, semisolid dosage forms | High temp. incineration 1200C
Limited quantity of untreated solids, semi solids, powders | Landfill
Diluted liquids (syrups), intravenous fluids | Sewer
HANDLING OF BIO MEDICAL WASTE
As per D &C Act and rules, handling & disposal should be done as per Biomedical waste (Management & Handling) Rules, 1998.
TREATMENT OF BIO MEDICAL WASTE
Sorting to separate other category of waste in separate area
Pack and store separately
Different color codes containers used for disposing
Containers should carry labels with prescribed information as per Sch. III & IV
Approved process of destruction & keep record of destruction by authorized person
Machines etc used for destruction should be sanitized regularly
Waste should not be kept for more than 48 hours

## Slide 27: Method To Dispose Bio Medical Waste
No. | Type of Waste | Method
1 | Human waste (Organs, tissues) | Incineration, deep burial
2. | Animal Waster | Incineration, deep burial
3 | Microbiological waste | Autoclave, Incineration
4 | Sharp wastes (blades, needle, syringes) | Disinfection (Chemical treatment or autoclave)
5 | Cytotoxic drugs | Incineration
6 | Solid waste (cotton, dressing, plaster) | Autoclave, Incineration
7 | Solid waste (tubings, catheters, I.V. sets) | Disinfection (Chemical treatment or autoclave)
8 | Liquid waste ( obtained from Washing, disinfecting process) | Disinfection (Chemical treatment or Discharge into drains)
9 | Incineration ash | Disposal in drains

## Slide 28: COLOR CODING FOR SEGREGATION OF BIOMEDICAL WASTE
COLOR | WASTE | TREATMENT
YELLOW | Human & animal anatomical waste/microbiology waste & soiled/ cotton/dressings/linen/beddings etc. | Incineration/ deep burial
RED | Tubing’s/catheters IV sets | Autoclaving/microwaving/ chemical treatment
BLUE/ WHITE | Waste sharps (needles, syringes, scapels, blades etc.) | Autoclaving/microwaving/ chemical treatment & destruction/ shredding
BLACK | Discarded medicines/ cytotoxic drugs, incineration ash, chemical waste | Disposal in secured landfill

## Slide 30: REFERENCES
Pharmaceutical Quality Assurance, Paul SD, Heswani G, Ed. 2019, S. Vikas and Company, Punjab.
New Concepts in Pharmaceutical Quality Assurance, Chakraborty AK, Manekar SS, Rathod SM, Ed. 2020, S. Vikas and Company, Punjab.
Pharmaceutical Quality Assurance, BP Nagori, A Gaur, R Solanki, V Mathur, 2018, Scientific Publishers Jodhpur.