## Slide 1
Learn how to draw configuration diagram
Step -1 : Define Scale
100 mm = 1.5 inch
D
C
1.5 inch
 | Actual dimension | Drawing dimension
AB | 60 mm | 0.9 inch
BC | 120 mm | 1.8 inch
CD | 100 mm | 1.5 inch
AD | 50 mm | 0.75 inch
CE | 80 mm | 1.2 inch
DE | 120 mm | 1.8 inch
EF | 150 mm | 2.25 inch
A
B
0.9 inch
1.8 inch
B
C
A
D
0.75 inch
C
E
1.2 inch
1.8 inch
D
E
2.25 inch
E
F
A
D
B
1200
How to locate point C?
From point D we draw an arc of radius 1.5 inch and from point B we draw an arc of radius 0.9 inch .These two arc where it intersect is point C

## Slide 2
Learn how to draw configuration diagram
A
D
B
1200
How to locate point C?
From point D we draw an arc of radius 1.5 inch and from point B we draw an arc of radius 0.9 inch .These two arc where it intersect is point C
This circle have radius CD and centre D.
This circle have radius BC and centre B.
C
A
D
B
1200
C
This circle have radius DE and centre D.
This circle have radius CE and centre C.
E

## Slide 3
Learn how to draw configuration diagram
A
D
B
1200
C
This circle have radius DE and centre D.
This circle have radius CE and centre C.
E
A
D
B
1200
C
E
This circle have radius EF and centre E.
F

## Slide 4
A
D
1200
C
E
F
B
 | Actual dimension | Drawing dimension
AB | 60 mm | 0.9 inch
BC | 120 mm | 1.8 inch
CD | 100 mm | 1.5 inch
AD | 50 mm | 0.75 inch
CE | 80 mm | 1.2 inch
DE | 120 mm | 1.8 inch
EF | 150 mm | 2.25 inch
60
120
100
50
80
120
150
Configuration Diagram

## Slide 5
Velocity analysis
A
D
B
1200
C
Given Speed of link AB
NAB = 100 rpm
Calculate angular speed of link AB
ωAB = (2 x 3.14 x NAB ) / 60 = 10.47 rad /s
Calculate the velocity of point B
Magnitude vB = ωAB x AB = 10.47 x 0.06 m = 0.628 m/s
Direction of velocity of point B is perpendicular to AB
Now define scale for drawing velocity diagram
Scale 0.628 m/s = 1 inch
A
D
B
1200
C
A
B
Perpendicular to AB
1 inch
a
b
D
C
Perpendicular to CD
This is the direction of velocity of point C
This is the direction of velocity of point B
Perpendicular to BC
This is the direction of relative velocity of C with respect to B
C
bc = relative velocity of C with
respect to B.
ca = absolute velocity of C.
Measure length bc and ca. then
Convert into proper scale yu will get velocity of point C and
Relative velocity of point C with respect to point B

## Slide 6
A
D
1200
C
E
F
B
 | Actual dimension | Drawing dimension
AB | 60 mm | 0.9 inch
BC | 120 mm | 1.8 inch
CD | 100 mm | 1.5 inch
AD | 50 mm | 0.75 inch
CE | 80 mm | 1.2 inch
DE | 120 mm | 1.8 inch
EF | 150 mm | 2.25 inch
60
120
100
50
80
120
150
Configuration Diagram
a
b
C
Velocity diagram
e
f
a
b
C
e
f
Velocity diagram

## Slide 7
a, d
b
C
e
f
Velocity diagram
Vector ab = velocity of point B
Vector bc = relative velocity of C with respect to B
Vector ca = velocity of C
Vector ae = velocity of point E
Vector af = velocity of point F
ab + bc = ac
cd + ce = ae
de + ef = af
Vb + Vc/b = VC
Vc + Ve/c = Ve
Ve+ Vf/e= Vf
ωbc = ( bc ) / BC
ωcd = ( cd ) / CD
ωef = ( ef ) / EF