## Slide 1: Practice problem-1 based on today class.

## Slide 2
Practice problem -1: In a slider – crank mechanism, the crank is 480 mm long and rotates at
20 rad/s in the counter-clockwise direction. The length of the connecting rod is 1.6 m. When the
Crank turns 600 from the inner-dead centre, determine the
Velocity of the slider (answer : 9.7 m/s)
Velocity of a point E located at a distance 450 mm on the connecting rod extended
(answer : 10.2 m/s)
(iii) Angular velocity of the connecting rod (answer: 3.28 rad/s clockwise)

## Slide 3
OA = 480 mm
AB = 1.6 m
Velocity of point A
Magnitude
VA = OA x ωOA
= 0.48 x 20
= 9.60 m/s
Direction
Velocity of A is perpendicular to OA
In OAB,
Angle B = 15.06 degree
Angle A = 180 – 60 – 15.06 = 104.94 degree
o
A
B
20 rad/s
600
1.6 m
15.060
104.940

## Slide 4
o
A
B
600
1.6 m
15.060
104.940
VA
75.060
14.940
VB
Velocity component of A along AB = VA Cos ( 14.940 )
Velocity component of B along AB = VB Cos ( 15.060 )
Velocity component of A along AB = Velocity component of B along AB
VA Cos ( 14.940 ) = VB Cos ( 15.060 )
VB = 9.6 x Cos ( 14.940 ) / Cos ( 15.060 ) = 9.605 m/s

## Slide 5
o
A
B
600
1.6 m
15.060
104.940
VA
75.060
14.940
VB
DIRECTION PERPENDICULAR TO AB
DIRECTION PERPENDICULAR TO AB
Velocity component of A perpendicular to AB
= VA Sin ( 14.940) = 9.6 x Sin ( 14.940)
Velocity component of B perpendicular to AB
= VB Sin ( 15.060) = 9.605 x Sin ( 15.060)
Angular velocity of Link AB = (VA Sin ( 14.940) + VB Sin ( 15.060) ) / AB = 3.11 rad/s

## Slide 6
Velocity of E along AB , Vex = Velocity of A along AB = Velocity of B along AB.
Velocity of A along AB ,VEx = = VA Cos ( 14.940 ) = 9.28 m/s
VA sin ( 14.940 ) =2.47 m/s
VB sin ( 15.060 ) =2.50 m/s
Vby = 2.5 m/s
VAy = 2.47 m/s
1.6 m
VEy
A
B
E
0.45 m
m/s
m/s
m/s