## Slide 1
CONSIDERATIONS FOR IN VITRO DISSOLUTION TESTING MODELS
Dr. Kalpana
School of Pharmaceutical sciences,
CSJMU
(22/4/22)

## Slide 2
Advantages of dissolution testing:
The major advantage of dissolution testing is that the rate of release and the extent of absorption of a drug is determined by the dissolution of the dosage form.
The dissolution test apparatus is robust and simple to use, requiring no specialist to handle.
It is well standardized and sufficiently flexible to allow perform testing for a broad range of oral solid dosage forms.
Dissolution testing is used to determine the quality of pharmaceutical products (tablets/capsules) based on the characteristics of in vitro release of the products.
Dissolution testing is used to establish the quality of pharmaceutical products, mostly tablets and capsules, based on the in vitro drug release characteristics of these products.
Dissolution testing of solid dosage forms plays a significant role in the decision-making process from a regulatory perspective, mainly in the development and approval of generic medicines, where it is possible to avoid unnecessary human studies without compromising the quality of pharmaceutical products.
The pharmaceutical manufacturer takes advantage of dissolution testing by using it to assess product development, product stability, quality control, and quality assurance, and to establish in-vitro-in-vivo correlation.
The dissolution apparatus can be easily automated which is important for routine investigations.

## Slide 3
Dissolution is a process in which a solid substance solubilizes in a given solvent i.e. mass transfer from the solid surface to the liquid phase.
Rate of dissolution is the amount of drug substance that goes in solution per unit time under standardized conditions of liquid/solid interface, temperature and solvent composition.
Factors to be considered while designing of a dissolution test
1. Factors relating to the dissolution apparatus
2. Factors relating to the dissolution fluid
3. Process Parameters

## Slide 4: 1. Factors relating to the dissolution apparatus
Design of the container
Size of the container
Shape of the container
Nature of agitation
Speed of agitation
Performance precision of the apparatus

## Slide 5
FACTORS RELATING TO THE DISSOLUTION FLUID
Volume
Temperature
Deaeration of dissolution medium
pH
PROCESS PARAMETERS:
Method of introduction of dosage form
Sampling Techniques
Changing the dissolution fluid

## Slide 6
There are basically three general categories of dissolution apparatus :
1. Closed-compartment apparatus
2. Open-compartment (continuous flow-through) apparatus
3. Dialysis systems
Closed-compartment apparatus :
Limited volume apparatus operating under nonsink conditions.

## Slide 7
OPEN FLOW-THROUGH COMPARTMENT SYSTEM
The dosage form is contained in a small vertical glass column with built in filter through which a continuous flow of the dissolution medium is circulated upward at a specific rate from an outside reservoir using a peristaltic or centrifugal pump.
Dissolution fluid is collected in a separate reservoir.
E.g. lipid filled soft Gelatin capsule

## Slide 8
ADVANTAGES
No stirring and drug particles homogeneous, laminar flow that controlled. All the problems of are exposed to can be precisely wobbling, shaft eccentricity, vibration, stirrer position don’t exist.
There is no physical abrasion of solids.
Perfect sink conditions can be maintained

## Slide 9
DISADVANTAGES
Tendency of the filter to clog because of the unidirectional flow.
Different types of pumps, such as centrifugal, have been shown to peristaltic and give different dissolution results.
Temperature control is also much more difficult to achieve in column type flow through system than in the conventional stirred vessel type.

## Slide 10
DIALYSIS SYSTEM
Here, dialysis membrane used as a selective barrier between fresh solvent compartment and the cell compartment containing dosage form.
It can be used in case of very poorly soluble drugs and dosage form such as ointments, creams and suspensions.

## Slide 11
Thank you