## Slide 1
IN VITRO DISSOLUTION TESTING MODELS
Dr. Kalpana
School of Pharmaceutical sciences,
CSJMU
(26/4/22)

## Slide 2: Need for Dissolution study
Evaluation of bioavailability
Development of more efficacious and therapeutically optimal dosage forms
Minimizes uses of humans as test subjects
Ensures quality of product
Correlation between dissolution results and bioavailability of product between batches
Product development , quality control and research and application
Screening of formulations during product development

## Slide 3: Official dissolution rate test apparatus
App no | I.P | B.P | U.S.P | Drug Product
1 | Paddle | Basket | Rotating basket | Tablets
2 | Basket | Paddle | Paddle | Tablets , capsules
3 |  | Flow through cell | Reciprocating cylinder | Extended release formulation
4 |  |  | Flow through cell | Low water soluble drug
5 |  |  | Paddle over disk | Transdermal formulation
6 |  |  | Rotating cylinder | Transdermal formulation
7 |  |  | Reciprocating disk | Extended release formulation

## Slide 4
ROTATING BASKET APPARATUS (APPARATUS 1)
First described by Pernarowski
It is basically a closed-compartment, beaker type apparatus.
It comprising of a cylindrical glass vessel with hemispherical bottom of one litre capacity partially immersed in a water bath.
A cylindrical basket made of #22 mesh is located centrally in the vessel at a distance of 2 cm from the bottom and rotated by a variable speed motor through a shaft.
All metal parts like basket and shaft are made of stainless steel.

## Slide 5
ROTATING PADDLE APPARATUS(APPARATUS 2)
First described by Levy and Hayes.
Here, basket is replaced with a paddle which acts as a stirrer.
A small, loose, wire helix may be attached to the dosage form that would otherwise float.
The position and alignment of the paddle are specified in the official books.

## Slide 6
THE RECIPROCATING CYLINDER METHOD (APPARATUS 3)
This method adopts the USP disintegration “basket and rack” assembly for the dissolution test.
The disks are not used.
This method is less suitable for precise dissolution testing due to the amount of agitation and vibration involved.
Used for dissolution testing of controlled-release bead-type (pellet) formulation.
Set of cylindrical , flat bottomed glass vessels equipped with reciprocating cylinders
For testing extended release products and beads
Temp 37oC

## Slide 7: Flow through cell method (apparatus-4)
Reservoir of medium
Pump that forcing medium throgh the cell holding test sample
Flow rate from 4-16 ml /min
For modified release dosage forms, containing active ingredients with limited solubility
Laminar flow by pulse less pump
Dissolution media may be fresh or recirculated

## Slide 8
PADDLE OVER DISK METHOD (APPARATUS 5)
Modification of Apparatus 2.
Here, stainless steel disk designed for holding transdermal system at the bottom of the vessel.
The disk/device should not , react with, or interfere with the specimen being tested.
The disk holds the system flat and is positioned such that the release surface is parallel with the bottom of the paddle blade.

## Slide 9
CYLINDER METHOD (APPARATUS 6)
Same as apparatus 1,except to replace the basket and shaft with a S.S. cylinder stirring element.
Temperature - 32 ± 0.5°
The dosage unit is placed on the cylinder.
Distance between the inside bottom of the vessel and cylinder is maintained at 25 ± 2 mm.
Used for transdermal formulation

## Slide 10
RECIPROCATING HOLDER METHOD (APPARATUS 7)
The assembly consists of a set of calibrated solution containers, a motor and drive assembly to reciprocate the system vertically.
Various type of sample holder are used.
Used for controlled-release formulation

## Slide 11
Thank you