## Slide 1: Biomedical waste Management-1
Dr. Versha Prasad

## Slide 2: Need for BMW management
BMW may have serious public health consequences and a significant impact on the environment!
WHO has estimated that. . . In year 2000, injections with contaminated syringes caused:
21 million hepatitis B virus (HBV) infections (32% of all new infections)
2 million hepatitis C virus (HCV) infections (40% of all new infections)
2.6 million HIV infections (5% of all new)

## Slide 3: STEPS INVOLVED-Segregation
• It refers to the basic separation of different categories of waste generated at source
• Reduces the risks and cost of handling and disposal
• Effective segregation alone can ensure effective bio-medical waste management

## Slide 4: Categories of BMW
Category | Type of Bag/container used | Type of waste
Yellow | Non-chlorinated plastic bags Separate collection system leading to effluent treatment system | a. Human anatomical waste b. Animal anatomical waste c. Soiled waste d. Expired or discarded medicines e. Chemical waste f. Micro, other clinical lab waste g. Chemical liquid waste

## Slide 5
Category | Type of Bag/container used | Type of waste
Red | Non-chlorinated plastic bags or containers | Contaminated waste (Recyclable) Tubing, bottles, IV tubes and sets, catheters, urines bags, syringes (without needles) and gloves
White | (Translucent) Puncture, Leak, tamper proof container | Waste sharps including Metals
Blue | Cardboard boxes with blue colored marking | Glassware

## Slide 6: Yellow Bin
Human and animal anatomical waste,
soiled waste,
expired or discarded medicines,
chemical solid and liquid waste, microbiology,
biotechnology and other clinical laboratory waste

## Slide 7: Red Bin
Contaminated Waste (Recyclable) Wastes generated from disposable items such as tubing,
bottles,
intravenous tubes and sets,
syringes (without needles and fixed needle syringes)
and vacutainers with their needles cut) and
gloves

## Slide 8: Blue Bin
Glassware Broken or
discarded and
contaminated glass including medicine vials and
ampoules except those contaminated with cytotoxic waste.

## Slide 9: White Container
Waste sharps including Metals Needles, syringes with fixed needles,
needles from needle tip cutter or burner, scalpels,
blades, or any other contaminated sharp object that may cause puncture and cuts.
This includes both used, discarded and contaminated metal sharps.

## Slide 10: BMW Pre-treatment (yellow category)
• On-site pre-treatment of laboratory waste, microbiological waste, blood samples, blood bags Methods
• Chemical disinfection
• Autoclave

## Slide 11: BMW Pre-treatment (yellow category)
Chemical/liquid waste
Some chemicals require pre-treatment before they can be safely disposed of by other types of disposal methods.
Liquid laboratory wastes that are commonly disposed of in the sink include used buffer solutions, neutralized acids and caustics, and very dilute aqueous solutions of water-soluble organic solvents (e.g., methanol, ethanol).
Any form of liquid waste should be diluted with at least a 100-fold excess of water or with a large excess of water up to 10 gallons.
Acids should be neutralised with an equal volume of a base and further diluted in water to flush into the sink.

## Slide 12: BMW Pre-treatment (yellow category)
Autoclaving Each autoclave should have graphic or computer recording devices which will automatically and continuously monitor and record dates, time of day, load identification number and operating parameters throughout the entire length of the autoclave cycle.
All records to be kept for 05 years.

## Slide 13: storage of BMW
The bags containing lab waste are brought for safe retention to the temporary storage facility till they are disposed off.
Transport
• Offsite transport is the carriage of health-care waste on the public streets away from a health-care facility
• Biomedical Waste from storage area is transferred to the common regional facility for BMW final disposal

## Slide 14: Important Biomedical Waste Management Rule
a. The scope of the rules has been expanded to include vaccination camps, blood donation camps, surgical camps or any other healthcare activity b. Phase-out the use of chlorinated plastic bags, gloves and blood bags within two years c. Pre-treatment of the laboratory waste, microbiological waste, blood samples and blood bags through disinfection sterilization on-site in the manner as prescribed by WHO

## Slide 15: Important Biomedical Waste Management Rule
d. Provide training to all its health care workers and immunize all health workers regularly.
e. Establish a Bar-Code System for bags or containers containing bio-medical waste for disposal.
f. Report major accidents
g. BMW has been classified in to 4 categories instead of 10 to improve the segregation of waste at source yellow, red, white and blue
h. No occupier shall establish on-site treatment and disposal facility, if a service of `CBMWTF is available at 75 km.
i. Operator of a CBMWTF to ensure the timely collection of bio-medical waste from the HCF and assist the HCF in conduct of training.