## Slide 1: Karnaugh Maps (K-map)
Alternate representation of a truth table
  Red decimal = minterm value
    Note that A is the MSB for this minterm numbering
  Adjacent squares have distance = 1
Valuable tool for logic minimization
  Applies most Boolean theorems & postulates automatically (when procedure is followed)
0 1
B A
0
1
0 | 1
2 | 3
2-variable K-Maps
B
0 | 1
2 | 3
A
form 1
form 2

## Slide 2: Karnaugh Maps (K-map)
Alternate forms of 3-variable K-maps
Note end-around adjacency
  Distance = 1
BC
A
00 01 11 10
0
1
0 | 1 | 3 | 2
4 | 5 | 7 | 6
Note: A is MSB, C is LSB for minterm 00 numbering
01
B
0 | 1 | 3 | 2
4 | 5 | 7 | 6
C
A
B
C
0 | 1
2 | 3
6 | 7
4 | 5
A
form 1
form 2
C AB
0 | 1
2 | 3
6 | 7
4 | 5
11
10
0 1

## Slide 3: K-mapping & Minimization Steps
Step 1: generate K-map
Put a 1 in all specified minterms
Put a 0 in all other boxes (optional)
Step 2: group all adjacent 1s without including any 0s
All groups (aka prime implicants) must be rectangular and contain a “power-of-2” number of 1s
  1, 2, 4, 8, 16, 32, …
An essential group (aka essential prime implicant) contains at least 1 minterm not included in any other groups
  A given minterm may be included in multiple groups
Step 3: define product terms using variables common to all minterms in group
Step 4: sum all essential groups plus a minimal set of remaining groups to obtain a minimum SOP

## Slide 4: K-map Minimization Example
Z=A,B,C(1,3,6,7)
  Recall SOP minterm implementation
    8 gates
27 gate I/O
K-map results
  4 gates
  11 gate I/O
BC
A
00 01 11 10
0
1
0 1 1 0
0 1
0 4
3 2
A | B C | Z | Row value
0 | 0 0 | 0 | 0
0 | 0 1 | 1 | 1
0 | 1 0 | 0 | 2
0 | 1 1 | 1 | 3
1 | 0 0 | 0 | 4
1 | 0 1 | 0 | 5
1 | 1 0 | 1 | 6
1 | 1 1 | 1 | 7
Z=AC + AB
A’C
AB
A’
A
C B
Note: this group not needed since 1s are already covered
5 0 1 7 6 1
essential prime implicants

## Slide 5: K-map Minimization Goals
Larger groups:
  Smaller product terms
    Fewer variables in common
  Smaller AND gates
    In terms of number of inputs
Fewer groups:
  Fewer product terms
    Fewer AND gates
    Smaller OR gate
      In terms of number of inputs
Alternate method:
  Group 0s
    Could produce fewer and/or smaller product terms
  Invert output
    Use NOR instead of OR gate

## Slide 6: 4-variable K-maps
Note adjacency of 4 corners as well as sides
Variable ordering for this minterm numbering: ABCD
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
D
form 2
C
B
A
form 1
CD
AB 00 01 11 10
00
01
11
10
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10

## Slide 7: 5-variable K-map
Note adjacency between maps when overlayed
  distance=1
Variable order for this minterm numbering:
  A,B,C,D,E (A is MSB, E is LSB)
00
01
11
10
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
A=0
01 11 10 01 11 10
00
01
11
10
16 | 17 | 19 | 18
20 | 21 | 23 | 22
28 | 29 | 31 | 30
24 | 25 | 27 | 26
BC DE 00 BC DE 00
A=1

## Slide 8: 5-variable K-map
Changing the variable used to separate maps changes minterm numbering
Same variable order for this minterm numbering:
  A,B,C,D,E (A is MSB, E is LSB)
00
01
11
10
0 | 2 | 6 | 4
8 | 10 | 14 | 12
24 | 26 | 30 | 28
16 | 18 | 22 | 20
E=0
01 11 10 01 11 10
00
01
11
10
1 | 3 | 7 | 5
9 | 11 | 15 | 13
25 | 27 | 31 | 29
17 | 19 | 23 | 21
AB CD00 AB CD00
E=1

## Slide 9: 6-variable K-map
Variable order for minterm numbers: ABCDEF
00
01
11
10
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
B=0
01 11 10 01 11 10
00
01
11
10
16 | 17 | 19 | 18
20 | 21 | 23 | 22
28 | 29 | 31 | 30
24 | 25 | 27 | 26
CD EF 00 CD EF 00
B=1
A=0
A=1
01 11 10
00
01
11
10
32 | 33 | 35 | 34
36 | 37 | 39 | 38
44 | 45 | 47 | 46
40 | 41 | 43 | 42
CD EF 00
01 11 10
00
01
11
10
48 | 49 | 51 | 50
52 | 53 | 55 | 54
60 | 61 | 63 | 62
56 | 57 | 59 | 58
CD EF 00

## Slide 10: Don’t Care Conditions
Sometimes input combinations are of no concern
  Because they may not exist
    Example: BCD uses only 10 of possible 16 input combinations
  Since we “don’t care” what the output, we can use these “don’t care” conditions for logic minimization
    The output for a don’t care condition can be either 0 or 1
      WE DON’T CARE!!!
Don’t Care conditions denoted by:
  X, -, d, 2
    X is probably the most often used
Can also be used to denote inputs
  Example: ABC = 1X1 = AC
    B can be a 0 or a 1

## Slide 11: Don’t Care Conditions
Truth Table
K-map
Minterm
Z=A,B,C(1,3,6,7)+d(2)
Maxterm
  Z=A,B,C(0,4,5)+d(2)
Notice Don’t Cares are same for both minterm & maxterm
BC
A
00 01 11 10
0
1
0 1 1 X
0 1
0 4
3 2
5 0 1 7 6 1
A | B | C | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | X
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Z=B+A’C
Z=AC + B
A’C
A’
A C
B
Circuit analysis:
G=3 GIO=8
(compared to G=4 & GIO=11 w/o don’t care)

## Slide 12: Design Example
Hexadecimal to 7-segment display decoder
  A common circuit in calculators
  7-segments (A-G) to represent digits (0-9 & A-F)
    A logic 1 turns on given segment
Hex to 7-segment decoder
In3 In2 In1 In0
A B C D F F
Circuit block diagram
7 segments
active (on) segments for a given HEX value
A
B
C
D
E
F
G
= don’t care

## Slide 13: HEX to 7-seg Design Example
Create truth table from specification
In3 In2 In1 In0 |  |  |  | A | B | C | D | E | F | G
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | X | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | X | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1
A
B
C
D
E
F
G
= don’t care

## Slide 14: HEX to 7-seg Design Example
Generate K-maps & obtain logic equations
In3 In2 In1 In0 |  |  |  | A | B | C | D | E | F | G
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1
00 | 01 | 11 | 10
1 | 1 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 1 | 0 | 1
01
11
10
A = In2’In0’ + In3’In1 + In2 In1
+ In3 In0’ + In3’In2 In0 + In3 In2’In1’
In1 In0 In3 In2
00
00 | 01 | 11 | 10
1 | 0 | 1 | 1
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
In1 In0 In3 In2
00
01
11
10
B = In2’In0’ + In2’In1’ + In3’In1’In0’
+ In3 In1’In0 + In3’In1 In0
K-map for A output
K-map for B output

## Slide 15: HEX to 7-seg Design Example
K-maps & logic equations for outputs C-G
00 01 11 10
1 0 0 1
0 0 0 1
1 1 1 1
1 0 1 1
00
01
11
10
In3 In2
00 | 01 | 11 | 10
1 | 0 | 0 | 0
1 | 1 | X | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
In1 In0 In3 In2
00
01
11
10
K-map for F output
00 | 01 | 11 | 10
0 | 0 | 1 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 1 | 1 | 1
In1 In0 In3 In2
00
01
11
10
K-map for G output
00 01 11 10
1 1 1 0
1 1 1 1
0 1 0 0
1 1 1 1
00
01
11
10
In3 In2
00 01 11 10
1 0 1 1
0 1 0 1
1 1 0 1
1 X 1 0
00
01
11
10
In3 In2
In1 In0 In1 In0 In1 In0
K-map for C output K-map for D output K-map for E output
C = In3 In2’ + In1’In0 + In2’In1’ + In3’In0 + In3’In2 D = In3’In2’In0’ + In2’In1 In0 + In2 In1’In0
+ In3 In1’ + In2 In1 In0’
E = In2’In0’ + In3 In2 + In1 In0’ + In3 In1
F = In1’In0’ + In3 In2’ + In2 In0’ + In3 In1 + In3’In2
G = In3 In2’ + In1 In0’ + In3 In0 + In3’In2 In1’ + In2’In1

## Slide 16: HEX to 7-seg Design Example
Remaining steps to complete design:
  Draw logic diagram (sharing common gates)
    Analyze for optimization metirc: G, GIO, Gdel, Pdel
      See next page for logic diagram & circuit analysis
  Simulate circuit for design verification
    Debug & fix problems when output is incorrect
      Check truth table against K-map population
      Check K-map groups against logic equation product terms
      Check logic equations against schematic
  Optimize circuit for area and/or performance
    Use Boolean postulates & theorems
  Re-simulate & verify optimized design

## Slide 17: HEX to 7-seg Design Example
In0
In0’
In2’ In0’ In3’
In1 In2 In1
In3
In0’
In2’ In1’
In3
In2’ In1’
In0 In3 In2 In1 In0’
In3’
In0
In3’
In2
In3 In1
G13
In0’
In3 In0 In2’
In1
In1’ In0’ In3’
In2’ In1’ In3’ In1’ In0’
G20
G21
G23
G24
G25
G26
A
G1 G2 G3 G4 G17 G18
G6 G7 G5 G10 G11
5+0 B
G1 G5 G19 G20 G21
D
C G22 G23 G24 G25 G26
E
G6
G1 G8 G9 G12
5+0 F
G11 G12 G13 G16
G6 G9 G14 G15 G27
Circuit Analysis
G = 38 GIO = 141
Gdel = 3 Pdel = 30
worst case path:
In0In0’G1 A
1+9
2+3 G1
2+1 G2
2+1 G3
2+1 G4
2+1 G5
2+3 G6
2+1 G7
2+1 G8
2+1 G9
2+1 G10
2+2 G11
2+2 G12
In2 2+1
2+1 G14
2+1 G15
2+1 G16
In2 3+1
In0 In3
3+1 G19
In3 In1’ 3+1
In0
In3’
3+1 G18 In1 3+1
In0’ In3’
In2 In1’
In2’
G17 In1 3+2
In0 In2
3+1 G27
6+0
5+0
4+0
5+0 G
5+0
Prop delay in gates #inputs + # loads
In3’
1+8
In2’
1+7
In1’
1+9
9
In1 3+1
In0
In3
In1’ In3’
In2’ 3+1 In0’
In2
In1’ 3+1
In0
2+1 G22
# loads on PIs 9
In3
9 In2
9 In1